## Slide 1
Claire Poppett, LBNL
Lead Fiber scientist, DESI
Notes: baryon acoustic oscillations (BAO) refers to regular, periodic fluctuations in the density of the visible baryonic matter of the universe. In the same way that supernova experiments provide a "standard candle" for astronomical observations,[1] BAO matter clustering provides a "standard ruler" for length scale in cosmology

## Slide 2: Outline
DESI science
Instrument walkthrough
Robotic Fiber Positioners
  The need for robotic fiber positioners
  Fiber positioning technology
  Status of testing

## Slide 3: Outline
DESI science
Instrument walkthrough
Robotic Fiber Positioners
  The need for robotic fiber positioners
  Fiber positioning technology
  Status of testing

## Slide 4
What is the expansion history of the universe?
Notes: The main question we’re trying to answer, is what kind of universe are we in? And this al depends on the amount of dark energy and dark matter in the universe. More matter than energy = closed, more energy than metter=open, same energy as matter=flat

## Slide 5: DESI Will Discriminate Between Dark Energy Models
CDR Fig. 2.1
Notes: DE equation of state parameter
omega describes the equation of state of dark energy and is a cosmological constant. If omega<-1/3, then the expansion is accelerating

## Slide 6: DESI on the Hubble Diagram
Expansion Rate
Measure wavelengths of target galaxies spectral features as they are redshifted
Δz = 0.0005•(1+z)  Δλ ~ 0.5 Å
Notes: Complicated system, 3 channels, 3 types of object

## Slide 7: LRG Targets
Expansion Rate
Luminous Red Galaxies
~4 x 106 goal
0.4 < z < 1.0
Notes: 4 million objects – 5000 fibers, 5 years

## Slide 8: ELG Targets
Expansion Rate
Emission Line Galaxies
~24 x 106 goal
0.7 < z < 1.6
Notes: Blue band resolution: 1500

## Slide 9: QSO Targets
Expansion Rate
Quasar Tracers
~1.6 x 106 goal
0.9 < z < 2.2
Notes: NIR band: Resolution 4000
mid band: Resolution > 3000

## Slide 10: Ly-α Forest Targets
Expansion Rate
Quasar Ly-α Forest
~0.6 x 106 goal
2.2 < z < 3.5
Notes: Higher redshifts using quasar ly-a forest – it’s why we’re so keen to hang onto the blue despite it being so much more difficult

## Slide 11: The BAO Distance Ladder
Claire Poppett, LBNL
Notes: BigBOSS would measure "baryon acoustic oscillations" (BAO) - regular
variations in the density of mass in the universe - which are evident in
the netlike tendrils and voids of visible galaxies and intergalactic gas.
Ordinary matter adds up to only five percent of the mass-energy in the
universe, but its large-scale distribution maps underlying invisible dark
matter, another 20 percent of the total, and echoes the minute temperature
variations of the ancient cosmic microwave background radiation (CMB).
Thus BAO's recurring peaks in density, from the CMB to the present,
represent marks on a standard ruler of the cosmos that can be used to its
measure expansion history from early times until now.

## Slide 12: Outline
DESI science
Instrument walkthrough
Robotic Fiber Positioners
  The need for robotic fiber positioners
  Fiber positioning technology
  Status of testing

## Slide 13: Galaxy image formed at focal surface

## Slide 14: Galaxy image formed at focal surface

## Slide 15: Position fiber to capture galaxy

## Slide 16: Fiber directs galaxy light to Spectrometer
5000 fibers on focal plate, each with independent positioner
10 three-channel spectrometers, each with 500 fibers

## Slide 17: Elements of DESI System

## Slide 18: Elements of DESI System
Prime Focus Corrector
Notes: Primary mirror is f/2.7

## Slide 19: Elements of DESI System
Prime Focus Corrector
Focal Plate

## Slide 20: Elements of DESI System
Prime Focus Corrector
Focal Plate
Fiber System
Fiber Positioner

## Slide 21: Elements of DESI System
Prime Focus Corrector
Focal Plate
Fiber Positioner
Spectrometer
360-660nm
R=1500
620-840nm
R=3000
800-980nm
R=4000
Dichroic Beamsplitters
Fiber System

## Slide 22: Major DESI Hardware
Fiber View Camera & Mount
New Upper Ring, Spider, Cage
Corrector, Focal Plane Assembly, Thermal Enclosure
Fiber Harness
Ten Spectrographs & Rack/Thermal Enclosure

## Slide 23: Atmospheric Dispersion Compensator
+
Atmospheric
Dispersion
Net ADC
Dispersion
=
Image
Dispersion
ADC2
Dispersion
ADC1
Dispersion
+
Atmospheric
Dispersion
Net ADC
Dispersion
=
Image
Dispersion
ADC2
Dispersion
ADC1
Dispersion
Notes: 60 degrees off zenith

## Slide 24: Atmospheric Dispersion Correction
Geometric raytrace shows eects of atmospheric dispersion on telescope point spread function. a) A heavily chromatically aberrated view of the sky 60 from zenith. Overall scale is 1m square, PSF exaggerated by factor of 106. This chromatic aberration is removed by rotating the ADC prisms 85 as shown in b). The dispersion being compensated here is 3 arcsec.

## Slide 25: Prime Focus Corrector
Function – gather broadband galaxy light, deliver well focused beam … nearly normal to the focal surface
Requirements
  Field of view: >3˚ linear
  Wavelength band: 360 – 980 nm
  Geometric, manufacturing, and alignment blur <19 μm RMS radius, field-averaged
  Tilt of chief ray: <1˚

## Slide 26: Focal Plate System
Function – capture galaxy light bundles from the corrector onto fiber optic tips
Systems
  Focal plate
  Guide sensors
  Focus sensors
  Illuminated fiducials
  Fiber positioners
  Fiber view camera

## Slide 27: Fiber System
Function – capture, transport, and deliver the corrector galaxy spots to the spectrographs with as little attenuation and f/# degradation as possible
~3 m
~33 m

## Slide 28: Spectrograph
Function – capture fiber output beam, disperse, and image with small point spread function to achieve required resolution
Item |  | Requirement
Spectral Requirements |  | 
Bandpass |  | 360 – 980 nm
FWHM Resolution (λ/Δλ) | 360nm < λ < 555nm | > 1500
 | 555nm < λ < 656nm | > 3000
 | 656nm < λ < 980nm | > 4000
Optical Requirements |  | 
End to End Throughput | λ = 360 nm | > 35%
 | 400nm < λ < 600nm | > 55%
 | 600nm < λ < 900nm | > 60%
 | λ = 980nm | > 50%
FRD Throughput |  | > 90%
Maximum RMS Radius |  | < 12 µm
95% Encircled energy diameter |  | < 110 µm
50% Encircled energy diameter |  | < 50 µm
Optics only
Optics + fiber + detector
3 arm design to cover wavelength range at the required resolution

## Slide 29: Spectrograph(cont.)
Blue Grating
in test mount
Measured Wavefront (-1 order)
<1/2 wave P-V
CAD Rendering of Model used to
develop camera interfaces

## Slide 30: Throughput

## Slide 31: Outline
DESI science
Instrument walkthrough
Robotic Fiber Positioners
  The need for robotic fiber positioners
  Fiber positioning technology
  Status of testing

## Slide 32: BOSS plus plate
Notes: MOVIE

## Slide 33: BOSS: 1000 fibres DESI: 5000 fibres
From BOSS to DESI
Notes: So that’s what we did with BOSS, but BigBOSS is bigger. Main difference is in the number of fibres

## Slide 34
The BOSS fibre plugging team
Notes: This is the fibre plugging team for BOSS, their first day on the job

## Slide 35
The BOSS fibre plugging team
Notes: And this is the fibre plugging team now! We can’t make them do a plug plate with 5000 fibres!

## Slide 36
Hire Foxcom?
Notes: Maybe we could hire FoxCon to do it

## Slide 37
Hire Foxcom?
Notes: They’re kinda busy

## Slide 38: Robotic fiber positioners
Pick and place robots (eg 2df at AAO)
Tilting Spines (eg Echidna on FMOS)
Rotating axis (eg LAMOST at Xinglong Station China)

## Slide 39: Desired Positioner Characteristics
Compact: 5000 fibers in 3° diameter FOV on a 815mm diameter focal plate.
Accurate, Fast: Position to within 5µm as quickly as possible with lowest total energy dissipated.
Reliable: Lifetime >250,000 reconfigurations.
Low mass: Minimize gravity sag of focal plate.
Low power: Maintain thermal stability of focal plate.
Fiber-friendly: Maintain fiber min bend radius >50mm.

## Slide 40: Positioner Kinematics
In-Plane motion
Spherical motion about a point
Yaw
Pitch

## Slide 41: Positioner Kinematics
Reference design is theta-phi
In-Plane motion
Spherical motion about a point
Yaw
Pitch

## Slide 42
Ø8 mm transfer gear
Ø6 mm DC-motor with gearhead
(mounted on Theta-stage transfer gear)
hollow shaft
cam
lever
flexure (mounted on flexure housing)
support arm
ferrule clamp
lever pivot (supported by flexure housing)
LBNL R-theta actuators
R-theta fiber positioner uses brushless DC motors.
Mechanical evolution:
  R-axis driven by cam and lever.
  R-axis driven by cord and spool.
  ‘Production’ version with minor mod’s plus rotation hard stops.
  Analog hall sensor (>60 effective counts/rev), best solution.
Notes: VIDEO

## Slide 43: LBNL th-phi: 10.4mm reference design
theta stop
Al theta coupler
stainless steel theta bearing cartridge (threads into focal plate)
phi gearmotor
Al aft cap/theta motor mount
electronics board (provided by us)
back end of theta gearmotor
black anodized, Al upper housing
black anodized, Al ferrule holder (prototype configuration)
stainless steel phi bearing cartridge
Bonded surfaces are masked from black anodizing, as needed.
stainless steel theta tube (precision tubing)
openings allow access to thread fiber and phi motor wires through here

## Slide 45
1. LBNL XY performance
Claire Poppett Shanghai Collaboration meeting 45

## Slide 46
LBNL XY testing procedure
SBIG CCD with macro lens and filter
Test actuator
Integrating sphere
Reference fibre
Actuator electronics
Fibre fed input light from LED

## Slide 47: Testing Mohawk positioning accuracy at LBNL
1st move
rms error = 52um

## Slide 48: Testing Mohawk positioning accuracy at LBNL
2nd move
rms error = 23um

## Slide 49: Testing Mohawk positioning accuracy at LBNL
10th move
rms error = 3um

## Slide 50: Comparison of positioning accuracy

## Slide 51
2. LBNL FRD testing procedure
Claire Poppett Shanghai Collaboration meeting 51

## Slide 52: Experimental Characterization

## Slide 53: Collimated FRD test
Collimated light at input angle
Output light azimuthally scrambled to make donut – radial scrambling is due to FRD so FWHM of donut shows performance

## Slide 54: Full cone FRD test – injection angle effects

## Slide 55: Collimated FRD test

## Slide 56: FRD over lifetime of th-phi positioner

## Slide 57: Status and Conclusions
Corrector Design is fixed and glass is being ordered
Lens manufacture of 1 3-arm spectrograph is underway
  May be used for prototype instrument next year
  Testing of prototype gratings has begun and all gratings meet specifications
Identified different technologies for robotic positioners with very little further testing required
  Selection will be made at the end of May