## Slide 1
Accelerator design for multi-TeV future colliders based on laser-plasma accelerators
Carl Schroeder
BELLA Center, ATAP
Lawrence Berkeley National Laboratory
Snowmass @ LBNL, December 10, 2021
WarpX
Work supported by the U.S. DOE, Office of Science, Office of High Energy Physics, under Contract No. DE-AC02-05CH11231

## Slide 2
electron plasma density
laser driver
particle beam
plasma wavelength
2
Laser-driven plasma accelerators:
ultra-high accelerating gradients
Laser-driven plasma accelerator
(in quasi-linear regime)
Wakefield (plasma wave) driven by the ponderomotive force of a resonant laser pulse in plasma
Focusing and acceleration provided by plasma wave
Plasma density n0~1017 cm-3 yields E~10 GV/m
Wakefield driven by high-power, short duration laser drivers
Compact coupling (< 1 m) of laser drivers using plasma mirrors
Main advantages of laser-plasma accelerator technology for collider applications:
  compact linac footprint (both accelerating plasma cell and drive laser beam)
  ultra-short bunches (few micron) = reduced beamstrahlung = collider power savings
Esarey et al., Rev. Mod. Phys. (2009)

## Slide 3
Ultrahigh (GV/cm) gradients experimentally demonstrated
Nakamura et al., Phys. Plasmas (2007)
L~3 cm
n ~3x1018 cm-3
1 GeV
2.9%
30 pC
1.7 mrad
Ti:Sapphire laser:
(0.8 um, 2 J, 40 fs, 10 Hz)
underdense plasma channel
PIC (WarpX – J.-L. Vay)
λp~20 um
Laser-plasma accelerator technology:
  compact accelerator footprint (>10 GV/m)
  ultra-short bunches (few micron bunches, < plasma wavelength)
~30 GV/m
E-field of plasma wave
laser
3

## Slide 4
Basic configuration of a laser-plasma-based linear collider
Preliminary/Strawperson designs have been produced to guide R&D
R&D focus has been on developing laser-plasma accelerator
No complete conceptual design is ready (laser technology is developing)
Linac: staged laser plasma accelerators:
4
Leemans & Esarey Phys. Today (2009)
Design (optimizing operational plasma density, ~1017 cm-3) yields 5 GeV/stage (100 stages/linac for 1 TeV):
    Geometric/average gradient = 2.3 GV/m
Time structure at IP:
    single bunches, separated by ~20 μs (~50 kHz)
Short (8.5 μm rms), shaped current distribution
    beamstrahlung reduction:
    𝞂z< β*
Key characteristics of a laser-plasma linear collider:
C. Schroeder et al. NIMA (2016)

## Slide 5
High-level parameters for e+/e- laser-plasma collider
5
Laser-plasma linear e-/e+ collider |  | 1 TeV | 3 TeV | 15 TeV
Beam energy | TeV | 0.5 | 1.5 | 7.5
Particle number (1E9) |  | 1.2 | 1.2 | 1.2
Beam power | MW | 4.4 | 13 | 65
Luminosity (1E34) | cm-2 s-1 | 1 | 10 | 50
Transverse. beam sizes at IP, x/y | nm | 50 / 1 | 10 / 0.5 | 4 / 0.25
IP beta function, β* | mm | 0.1 | 0.1 | 0.1
RMS bunch length | micron | 8.5 | 8.5 | 8.5
Repetition frequency | kHz | 47 | 47 | 47
Time between collisions | microsec | 21 | 21 | 21
Beamstrahlung photons/e- |  | 0.6 | 1.4 | 1.6
Length (2x main linac tunnel) | km | 0.44 | 1.3 | 6.6
Facility site power (2 linacs) | MW | 105 | 315 | 1100
Upgrade potential: Same laser systems (linac) for 1, 3, and 15 TeV
Notes:
LWFA parameters:
1 um laser wavelength
1017 cm-3 plasma density

## Slide 6
High energies (1-15 TeV) accessible in conventional accelerator facility footprint
Plasma-based collider using ILC infrastructure
6
ILC upgrade:
  Replace SCRF with LWFA stages
  Laser drivers (~m2) and plasma cells fits in ILC main linac tunnel
  300 MW site power could support √s = 3 TeV LWFA design
  12 MW beam power for √s = 3 TeV LWFA design (ILC beam dumps rated for 17 MW)
ILC TDR

## Slide 7
R&D timeline towards a collider
DOE HEP AAC Roadmap (2016)
  US AAC community outlined R&D goals in 2016 roadmap
  Progress on all R&D goals
  Roadmap to be updated
7
R&D CDR TDR
Construction
5 10 15 20 25 30
  Technically-limited timeline:
years

## Slide 8
Laser technology requirements for a collider
Laser drivers:
Requires R&D to reach collider parameters:
10 J, 100 fs class, 50 kHz, high wall-to-laser efficiency
Two promising laser architectures:
  Coherent combination of fiber lasers (1 um). R&D at Jena, Michigan, LBNL, LLNL, et al.
      ~60% wall-to-laser efficiency
  Tm:YLF (1.9 micron) – (4x as many LWFA stages). R&D at LLNL
  Peak laser power requirements may be relaxed by excitation using laser pulse trains
8
BELLA (LBNL)
HAPLS (ELI)
CoReLS (Korea)
fiber
kBELLA
Tm:YLF
fiber
peak laser power [TW]
average laser power [kW]
collider
requirement:
50 kHz
> 40% effic.
technically
feasible
today: kHz
existing
laser
systems:
few Hz
2µm – 4xstages
Facilities needed to develop high-rep-rate technology (plasma targetry, diagnostics, etc.) and develop collider subsystems
High-average power laser drivers
1 um
10 pulse train
J. Cowley et al. PRL (2017)

## Slide 9
Mid-term collider options for Science and Accelerator R&D
9
𝛾 e , 𝛾𝛾
~10 years
Modest R&D required
~20 years
Significant R&D required
~15 years
e+e- (or 𝛾𝛾)
√s = 1 TeV (upgrade to 3 TeV, 15 TeV)
e- fixed target / high-intensity laser
collision
Accelerator:
Science
opportunities:
?
10 – 50 GeV; 1 kHz (upgrade 10 kHz)
√s = 16 – 80 GeV; 1 kHz (upgrade 10 kHz)
Lum~2x1030 cm-2s-1 (upgrade ~2x1031 cm-2s-1)
Requires development of scatter laser source (FEL)
e+ e-
√s = 20 – 100 GeV; 1 kHz (upgrade 10 kHz)
e+ plasma acceleration R&D required
Development of e+ source; damping ring
50 kHz
L = 1034 (upgrade to 1035)
e- e-
√s = 20 – 100 GeV ; 1 kHz (upgrade 10 kHz)
e-polarized
Lum= 4x1030 cm-2s-1 (upgrade 4x1031 cm-2s-1)
Higher lum. (~1032 cm-2s-1) without polarization
?
?
Next talks

## Slide 10
Summary
Laser-plasma collider concepts have potential to extend reach of linear lepton colliders to 15 TeV (at 5E35 luminosity)
  High gradients – extend energy reach
  Short beams – reduce beamstrahlung & save power
Community organizing toward integrated design study
  Potential to re-use collider facilities (e.g., ILC) to extend energy reach
Low energy demonstrators required to advance technology
  Science opportunities needed to motivate test facilities
10

## Slide 11
Backup slides

## Slide 12
Status of laser-plasma-accelerator experimental R&D
  Single stage achieved multi-GeV acceleration: 8 GeV in 20 cm (40 GV/m)
divergence:
150 mrad
  1 Hz rep. rate
  Reproducibility limited by laser fluctuations (at ~100 Hz)
discharge-capillary plasma waveguide
12
2019 (LBNL)
2014 (LBNL)
2006 (LBNL)
Energy gain (GeV) in LWFA stage
Operational plasma density (x1018 cm-3)
Gonsalves et al. PRL (2019)
  Proof-of-principle staging of plasma accelerators:
Compact driver coupling using plasma mirrors
  Proof-of-principle experiment demonstrate 100 MeV energy gain
  Multi-GeV staging experiments are planned / commissioning ongoing
Plasma lens focusing of beam
Steinke et al. Nature (2016)
2013 (TPW)
2013 (GIST)