## Slide 1
March 30, 2022
D. Ratner
SLAC National Accelerator Laboratory
Machine Learning Applications at SLAC

## Slide 2
Introduction to SLAC
LCLS-II
Particle accelerators for x-ray science
Vera Rubin Observatory
Cryo-EM facilities for COVID research
SLAC’s mission revolves around major scientific facilities
Research projects across biology, chemistry, geology, physics, energy sciences, materials science, and more

## Slide 3
Outline
Online control of x-ray facilities
Ghost imaging
ML for inverse problems
(But there are also many other applications across SLAC)

## Slide 4
Introduction to X-ray Free-Electron Lasers (XFELs)
Suga et al.
Photosystem II
Shock waves in extreme conditions
Milathianaki et al.
Si
Ekeberg et al.,
Single particle imaging (Mimivirus)
X-ray free-electron lasers: Accelerator driven x-ray sources to study ultrafast, ultrasmall scale phenomena

## Slide 5
Online optimization
XFEL tuning:
XFELs are instabilities  very sensitive to initial conditions
In total 500 hours/year on single task of quad tuning
Badger
optimizer
Automate (e.g. simplex)
Quadrupole magnets
FEL power

## Slide 6: Online optimization
Acquisition point
Acquisition
function
Ground truth
Posterior
Model-based optimization
Gradient optimizer
Advantage 1: Balance “exploitation vs. exploration”
 Find global maximum
Bayesian optimizer
Mitch McIntire

## Slide 7: Online optimization
Measured
Modeled
Quad 1
Quad 1
Quad 2
Advantage 2: Existence of model enables use of physics, archived data
Model-based optimization
ρ = 0.7
ρ = 0
Groundtruth
Model,
no correlation
Model,
w/ correlation
e.g. learning correlations in data improves modeling
Bayesian Optimization of a FEL, Duris et al., PRL, 2020

## Slide 8: Online optimization
Model-based optimization
Example 2: tuning quadrupoles from pure noise
Example 1: Fast tuneup in high dimensions
Upshot:  Faster tuning (factor of 4 vs. simplex)
 More robust tuning (e.g. tune from noise)
Bayesian Optimization of a FEL, Duris et al., PRL, 2020
4 parameters
Joe Duris, Dylan Kennedy

## Slide 9: Online optimization
Beam size measurement
Tuning param (e.g. solenoid)
Measurement parameter
(e.g. matching quadrupole)
Beam size measurement
Tuning param (e.g. solenoid)
Measurement parameter
(e.g. matching quadrupole)
Current focus on complex tasks: multi-objective, hysteresis, etc.
 InfoBAX: https://willieneis.github.io/bax-website/
W. Neiswanger et al., ICML, 2021
W. Neiswanger, S. Miskovich, A. Edelen
Calculate emittance
e.g. consider emittance optimization, i.e. beam quality

## Slide 10
Online optimization
Move optimization target downstream  tuning on user signals
Quadrupole magnets
FEL power
Hutch detectors
Ground truth
Adaptive
Raster
J. Betterton et al., ICRA, 2020
XRF Imaging
Phase mapping
Growing portfolio of anomaly detection…

## Slide 11
Outline
Online control of x-ray facilities
Ghost imaging
ML for inverse problems

## Slide 12: Ghost Imaging
Riddle: How can I take a picture with a spectrometer?
Answer: Have a friend with a flashlight
Ghost imaging / Single pixel camera / Compressive Sensing

## Slide 13: Ghost Imaging
Radiation, a
Target, x
b = [ 5037,
4783,
4891, … ]
Bucket measures total transmission
Classic GI formalism:
Raster scan
Ghost imaging
1. Fellgett’s/Multiplex advantage
Reconstructed Target, x*
Note: Valid for Gaussian read-out noise but not Poisson noise!
M. Harwit and N. Sloane, “Hadamard Transform Optics, Chapter 4: Noise or When to Multiplex and When to Avoid It,” 1979

## Slide 14: Compressive sensing
Compressive sensing concept:
Why record 660k points if only 39k needed?
Wikimedia
Trick: Use “prior” information to reconstruct the sample
e.g. Sky is uniform blue  minimize “total variation” of image

## Slide 15: Ghost Imaging
2. Compressive sensing formalism:
Radiation, a
Target, x
b = [ 5037,
4783,
4891, … ]
Bucket measures total transmission
Raster scan
Ghost imaging
1. Fellgett’s/Multiplex advantage
Reconstructed Target, x*
=
b
x
a
3. Measurement can be easier/better than control
Note: Multiplexing can reduce # of samples but not dose!

## Slide 16: Ghost Imaging
photocathode quantum efficiency
Cathode
target
K. Kabra, et al., Phys. Rev. Accel. Beams 23, 022803
DMD
Cathode laser
Ground truth
Reconstruction
Pegasus, UCLA

## Slide 17: Ghost Imaging
Simulated
Ground truth
Reconstruction
photocathode quantum efficiency
Cathode
target
Natural laser jitter
Day 1
Day 3
K. Kabra, et al., Phys. Rev. Accel. Beams 23, 022803 (2020)
Real data at LCLS
(no ground truth)
DMD
Cathode laser

## Slide 18: Ghost Imaging
Signal determined by probability of two photons separated by time d
d1
d2
d3
=
b
x
a
Electron spectra
X-ray autocorrelation
Sample dynamics
Pump X-ray
Sample, CO
Probe X-ray
e-
d
“Pump-probe” scan of delay, d
D. Ratner et al., PRX (2019)
T.J. Lane, D. Ratner Opt. Exp. (2020)

## Slide 19: Ghost Imaging
Spectral ghost imaging
Note that we never actually need power, only autocorrelation!
From Wiener-Khinchin theorem:
Electron bins
X-ray spectra
Time dynamics!
Spectral power:
Pump X-ray
Sample, CO
Probe X-ray
e-

## Slide 20: Ghost Imaging
Spatial domain
K. Kabra et al., PRAB (2020)
Probe: cathode laser jitter
Bucket: total charge (BPM)
Goal: monitor QE passively during operation
Biggest XFEL advantage: Measurement vs. control
Spectral domain
TJ Lane, Opt. Express, 28 (5) 2020
Probe: SASE bandwidth
Bucket: user signal
Goal: Probe narrow bandwidth without active control
Time domain
t
“Pump-probe” scan of delay, t
Probe: SASE spikes
Bucket: user signal
Goal: Probe short time scales without active beam control
D. Ratner et al., PRX (2020)

## Slide 21: Ghost Imaging
Ghost Imaging Summary
Felgett’s/Multiplex Advantage: Boost signal to noise ratio
Compressive sensing: converge to solution faster using priors
‘Measurement beats control’: Use what nature gives you for easier, faster, higher resolution measurements
Sample dose reduction is NOT an advantage of multiplexing
Felgett’s advantage does NOT work for Poisson detectors
T.J. Lane, D. Ratner, “What are the advantages of ghost imaging? Multiplexing for x-ray and electron imaging,” Opt. Exp., 2020
A. Kingston et al., “Inherent dose-reduction potential of classical ghost imaging,” PRA, 2021

## Slide 22
Outline
Online control of x-ray facilities
Ghost imaging
ML for inverse problems

## Slide 23: Deep Learning for Inverse problems
Generic inverse problem:
F
?
1. Solve optimization problem:
2. Train a neural network:
x
y
3. Train a cycle-consistent neural network:
X
Inputs
Y
Target
x
Y
F
Caveat: F must be differentiable!

## Slide 24: X-ray Pulse Reconstruction
Input power points
(3fs FWHM resolution)
Input spectral power points (80meV FWHM resolution)
Maxwell, Timothy J., et al. International Society for Optics and Photonics, 2014.
power
Spectrum
Measure amplitude of power/spectrum: can I recover phase?

## Slide 25: X-ray Pulse Reconstruction
Input power points
(3fs FWHM resolution)
Input spectral power points (80meV FWHM resolution)
Maxwell, Timothy J., et al. International Society for Optics and Photonics, 2014.
power
Spectrum
Measure Power
Measure Spectral power
Guess
Field
F(t),F(w)
F
Approach #1: Iterative optimization

## Slide 26: X-ray Pulse Reconstruction
Measure Power
Measure Spectral power
Guess
Field
F(t),F(w)
…
106-109 times
Pulse #1
Pulse #n
F
Approach #1: Iterative optimization

## Slide 27: X-ray Pulse Reconstruction
Problem: absolute phase is meaningless!
SimulatedInput
power
Spectrum
Labeled loss,
Predicted Output
Simulated Output
field
field
NN Inverse Model
Approach #2: Train a labeled neural network
D. Ratner et al., Opt. Exp., 2021

## Slide 28: X-ray Pulse Reconstruction
Input
power
Spectrum
power
Spectrum
Predicted Input
Predicted Output
Physics forward model, F
field
“Physics-informed neural network” (PINN)
Advantages: No need for labeled data, train directly on experimental data
NN Inverse Model
F
D. Ratner et al., Opt. Exp., 2021
Approach #3: Train a neural network with cycle-consistent loss
Unlabeled loss,

## Slide 29: X-ray Pulse Reconstruction
Inverse problem: Full beam reconstruction
Advantages: 108 faster, higher accuracy on amplitude and phase compared to iterative method
D. Ratner et al., Opt. Exp., 2021

## Slide 30: Cryo-EM Introduction
Youssef Nashed
Frederic Poitevin
Julien Martel
Axel Levy
Harshit Gupta
Geoffrey Woollard
Michael Kagan
Chun Hong Yoon
Daniel Ratner
SLAC/Stanford
    CryoPoseNet: End-to-End Simultaneous Learning of Single-particle Orientation and 3D Map Reconstruction from Cryo-electron Microscopy Data

## Slide 31: Cryo-EM Introduction
    CryoPoseNet: End-to-End Simultaneous Learning of Single-particle Orientation and 3D Map Reconstruction from Cryo-electron Microscopy Data
Youssef Nashed
Frederic Poitevin
Julien Martel
Axel Levy
Harshit Gupta
Geoffrey Woollard
Michael Kagan
Chun Hong Yoon
Daniel Ratner
SLAC/Stanford

## Slide 32: Deep learning for Cryo-EM Single Particle Imaging
Recast as an inverse problem:
Density map
Pose
F
Iteratively solve for pose and densities (e.g. expectation-maximization)
Why use deep learning?

## Slide 33: Deep learning for Cryo-EM Single Particle Imaging
Recast as an inverse problem:
Density map
1. Scaling with particle number: classical methods require pose for every particle
Pose
F
Iteratively solve for pose and densities (e.g. expectation-maximization)
Why use deep learning?

## Slide 34: Deep learning for Cryo-EM Single Particle Imaging
Recast as an inverse problem:
Density map
Iteratively solve for pose and densities (e.g. expectation-maximization)
1. Scaling with particle number: classical methods require pose for every particle
2. Solving for conformations: classical methods cannot handle complex, continuous variation
F
Pose
Why use deep learning?

## Slide 35: Deep learning for Cryo-EM Single Particle Imaging
Recast as an inverse problem:
CryoDRGN
Iteratively solve for pose and densities (e.g. expectation-maximization)
Why use deep learning?

## Slide 36: CryoPoseNet
Our architecture follows auto-encoder architecture:
Encoder network
Decoder network
Conformation Space
Orientation Space
Microscope Simulation
Input
Output
Forward model
Latent representations
Learn network/model parameters by minimizing the difference between input and output images
End-to-end differentiable forward model
The number of learned variables independent of data size
Pose estimation uses single pass through the encoder network
Explicitly decouple conformation and orientation space through the forward model

## Slide 37: CryoPoseNet
Our architecture follows auto-encoder architecture:
Synthesized E.coli adenylate kinase cryo-EM datasets
Each with 9000, 128x128 images and different SNRs
Pixel size of 0.8A
Reconstruction performed using Tensorflow in python
Youssef Nashed, Fred Poitevin, et al. ICCV (2021)

## Slide 38: CryoPoseNet
Nashed, Youssef SG, et al. arXiv preprint arXiv:2107.02958 (2021)
Our architecture follows auto-encoder architecture:
Euler
Quaternions
S2 x s2
Orientation MAE (degrees)
1. Pose estimation
F. Poitevin
Youssef Nashed, Fred Poitevin, et al. ICCV (2021)

## Slide 39: CryoPoseNet
Our architecture follows auto-encoder architecture:
RMSD
Youssef Nashed, Fred Poitevin, et al. ICCV (2021)

## Slide 40: Conclusion
Thanks to work by (among others):
F. Christie, E. Cropp, J. Cryan, J. Duris, A. Edelen, C. Emma, K. Kabra, A. Kennedy, T. J. Lane, S. Li, A. Lutman, G. Marcus, P. Musumeci, Y. Nashed, F. Poitevin, G. Stupakov, G. Wetzstein,
Thanks for listening!