## Slide 1: Advanced controls for coherent addition of femtosecond laser pulses
Russell Wilcox, Qiang Du, Dan Wang, Tong Zhou, Siyun Chen, Lauren Cooper

## Slide 2
Outline
Motivation
Principles of interferometer and phase detector
Pattern recognition for phase control
Femtosecond pulse diffractive combination
Conclusions and future work

## Slide 3
Accelerators need high power pulsed lasers
Laser parameter | Funded, ongoing | k-BELLA | Hi rep-rate driver | Collider driver
Energy | 0.2 J | 3J | 3J | 6J
Pulse duration | 30fs | 30fs | 30fs | 100fs
Rep-rate | 5 kHz | 1kHz | 10kHz | 50kHz
Average power | 1kW | 3kW | 30kW | 300kW
...to 50kHz
These lasers don’t exist, need a completely new laser technology
Leemans & Esarey,
Physics Today (2009)
From 1Hz...
Planned milestones:
Higher experimental data rate
Faster feedback to control error sources

## Slide 4
Fiber lasers have high power, limited energy
Light guided by high index core
Add laser ions, pump light; it’s an amplifier
Core is small
  Max diameter ~100um
Advantages:
  Average power
  Efficiency
  Bandwidth
  Beam quality
  Reliability
Limited energy due to
  Damage
  Nonlinearity
  Small volume
Beam combination can increase output energy
120 kW
1kW, 250fs
45% WPE
300 kW

## Slide 5
Various groups have combined ~100 beams
Chang et al, ASSL 2020 107 beams
Redmond et al, CLEO 2011. 200 beams
Fsaifes et al, Phot. West 2020, 60 beams
Du et al, Opt. Exp. 2021, 81 beams
tiled, spectral,
Our beam combiner will be a ~100-arm Mach-Zehnder interferometer

## Slide 6
Mach-Zehnder interferometer
LASER
beam
splitter
beam
splitter
mirror
mirror
path length
adjustment
additional pi
phase shift
on reflection
equal
phase
fields add
fields cancel

## Slide 7
Add amplifiers, it’s a combiner
LASER
beam
splitter
beam
splitter
mirror
mirror
path length
control
D
laser
amplifier
feedback
electronics
twice the output of one amplifier

## Slide 8
Detecting phase from intensity
interference term
LASER
+∏
-∏
0
detected power
0 to 2

## Slide 9
Dithering to disambiguate retrieved phase
+∏
-∏
0
detected power
+∏
-∏
0
detected power
“dither”
?

## Slide 10
At low rep-rate, control bandwidth is limited
repetition rate,
highest sampling frequency
need to suppress noise
below this frequency
Want to derive phase error
and control as fast as possible!

## Slide 11
Clever dither schemes for many beams
LOCSET
Dither each beam at a different frequency
Detect output, pick out each frequency with a filter, feed back to each beam
Advantage: lots of information
Scaling problem:
  For N beams, need N frequencies within narrow bandwidth
  Narrow bandwidth filter is slow to change (time/bandwidth product is constant)
SPGD
Add random dither value to all beams
Did that increase combined power?
    No: dither in different direction
    Yes: dither in same direction
Return to 2
Advantage: simple detection
Scaling problem:
  Single sensor, information bottleneck
  Number of iterations to optimize N beams scales as 10xN
  At optimal phase, sensitivity becomes zero; has to stabilize away from optimal
  Always dithering, noisy
Locking of optical coherence via single detector electronic frequency tagging
Stochastic parallel gradient descent

## Slide 12
Obtain phase using two interferometers
Iin
D
D
“in-phase”
“quadrature”
sine
cosine
No dithering, stable output, immediate data

## Slide 13
phase = pi/2 on other side
phase = 0 on one side
Quarter rotation between left and right sides.
Can start from any position, go forward or backward.
Quadrature phase concept is not new

## Slide 14
Diffractive splitter/combiner
Surface relief on transparent substrate.
Calculated to diffract coherent light toward an arbitrary spot pattern.
Arbitrary spot pattern
(input to calculation)
Coherent light source
LASER
Diffractive optical element (DOE) can split light into any pattern of rays
Also works in reverse

## Slide 15
We will use DOE combiner for hi-power beams
Splitter operated in reverse
Many beams into one element
High 90s splitting efficiency
High power (multi-kW)
5kW, 5 beams CW
Flores et al, Opt. Eng. 55, 096101 (2016)
Our 3x3 setup
DOE

## Slide 16
Side beams form an interference pattern
Side beams fluctuate in intensity as phases drift
Enough info to identify phase errors
Combined and side beams scale together
  With N inputs, (2N – 1) side beams (in each direction)
  Information thus scales with N, helping feedback rate
side beams are still there

## Slide 17
00
01
02
10
20
21
12
22
01
02
21
22
Some side beams give which-way info
correlations reveal quadrature phase!
“phase function” or “phase state”

## Slide 18
Control based on quadrature subset works
unlocked
locked
time, seconds
intensity, a.u.
0 10 20 30 40 50 60 70
Du et al, Opt. Lett. 44, 4554 (2019)
0.2% RMS stability
93% of theoretical efficiency
side beams with only 2 contributors:
Does this simple case scale to 100?

## Slide 19
Main plus side beams result from input beams convolved with DOE function
Phases drift, amplitudes not so much.
Efficient combination when:
Complex valued matrix convolution:
input beam phases equal DOE phase function,
but in reverse, because it’s combining, not splitting
General representation of DOE combination

## Slide 20
Measuring the phase function of a large DOE
SLM pixel values:
For measuring larger DOE phase function
SLM “programmable hologram” makes beam array easy
SLM controls all degrees of freedom of each beam
  Except polarization
Phase is controlled by shifting grating lines
Du et al, Opt. Exp. 29, 5407 (2021)

## Slide 21
Deriving the 9x9 DOE phase function
Note symmetry
  Invariant when rotated 180 about out-of-plane axis, like letter “S”
  Same asymmetric function in x and y?
Scan relative phase of two beams in x, two in y
Find all the power curves
Find phases with respect to scan phase
Yields the full DOE phase function

## Slide 22
Measured 9x9 phase and power function
We will input this to the DOE
Note symmetry of phase function is “S-like”
  With a minus sign
Same symmetry as in interference patterns

## Slide 23
Why the phase function is (a)symmetric
DOE phase function matched with its compliment, amounts to autocorrelation
Want autocorrelation to yield narrow spike (combined beam)
Such a function tends to be asymmetric, random-looking
  Thus, probably useful “quadrature-like” phase shifts always available for control! (This was a potential issue.)
Calculation of DOE finds the same optimal function for x and y
This results in “S” type symmetry of 2D pattern
Leger et al, Appl. Opt. 26, 4391 (1987)

## Slide 24
Input compliment of phase function to combine
Min. contrast 18dB
Ideal 9x9 DOE model
Min. contrast 20dB
Realistic 15x15 DOE model
60.4% eff, DOE is 72%
not optimized
Works in forward direction, but can’t be reversed to find phase errors for stabilization
In real laser, phases are unstable, so perfect inverse phase function is unavailable
  Need to actively control a complex array of beams
Simulated
Experimental

## Slide 25
Laser System
Phase Error
Measurement
Sensor
Phase Controller
A machine can find patterns in complex data
SPGD or Phase retrieval
SPGD or Phase retrieval
Phase Errors (input lasers)
Intensity Pattern (from camera)
Neural Network (NN)
Wang et al, Opt. Exp. 29, 5694 (2021)

## Slide 26
Phase error training range has to be < ± π/2
Trained outside ±π/2, it gets confused by non-unique correlations
  Maybe less-than-optimal phase shifts available
Works fine when trained in limited range
trained on full range
trained on limited range
Predictions of phase from trained NN:

## Slide 27
Examples of ambiguous patterns
Two patterns can have nearly identical side beam powers, completely different phases
Maybe restricting the training range can avoid this

## Slide 28
Small training range still works
Anywhere in phase space, better-than-even chance NN guesses the right direction to go next
Phase state random walks, but with a bias toward training range
Inside training range, one step to optimal
Maybe recognizing pattern similarities is enough
0 π 2π 3π

## Slide 29
How to initially put training range near optimal
Use the SPGD algorithm to stay near optimal, while exploring a little
No special phase-mapping knowledge needed for this to work
Dither process provides a set of input errors to learn
180 160 140 120 100 80 60 40 20
accuracy
Du et al, Opt. Exp. 30, 12639 (2022)
dither
range

## Slide 30
Results: full perturbation range
Prediction accuracy usually accumulates
phase difference from optimal
Wrong predictions
delay convergence
Simulation:

## Slide 31
Faster than SPGD at same sample rate
81 beam combiner simulation
SPGD steps scales as 10 x N
  10 x 81 ≈ 800
  OK if reprate >> error frequency
    For us, reprate ≈ error frequency
Pattern recognition scheme scales as √N
  Average to converge:
    8 beams: 5 steps
    81 beams: 40 steps
Better efficiency, stability (no dither)

## Slide 32
How to train on an unstable system?
pattern difference
drift over 24 hours, with same programmed inputs
Even with highly stable SLM setup, phases and powers drift:
The NN will have to be trained on real combiners with constantly changing parameters
Need a training scheme robust against drift

## Slide 33
NN (X) = Y
X
Y
NN
X = pattern before + pattern after dither
Y = dither
Before
After
dither
input
NN operation:
X = current pattern + target pattern
Y = correction
Current
Target
X
Y
NN
Phase Space
correction
Phase Space
Pattern
Space
NN training:
+
+
Pattern
Space
combiner
combiner
Differential learning/control is robust vs. noise
Wang et al, IEEE JQE 58, 6100309 (2022)

## Slide 34
NN trained differentially is efficient, stable
0.4% RMS over >30min
Combining efficiency: 78.1%
DOE splitting efficiency: 82.1%
Ratio: 0.95
Measured.gif
Power
Control variables
Du et al, Opt. Exp. 30, 12639 (2022)

## Slide 35
3 by 3 DOE
8 input beams
5 by 5 interference pattern
AI found the same important beams we did
Assigning humans the stabilization task:
“These eight beams should give enough information” (based on physics).
Stabilization worked.
Assigning AI the stabilization task:
“These eight beams are more informative than the others” (based on experience).
Stabilization worked.
Could AI be used to find important parts of complex data before they are understood?

## Slide 36
Control concept extends to temporal combining
Similar problem: patterns due to interference
Patterns are temporal (pulse trains), recognizable by NN
Stabilizes round trip phase in energy storage cavities
Pattern
data
Input pulses
Combined output
Phase
stabilizer
Wang et al, IEEE JQE 58, 6100309 (2022)

## Slide 37
With short pulses, need to cancel pulse front tilt
Angular dispersion (pulse front tilt) causes loss
  Compensate using second grating
Spatial and temporal dispersion still present
  Minimize by small diffraction angles
DOE
DOE2
(diffractive splitter in reverse)
DOE1
(integrated grating array)
Zhou et al, Opt. Lett. 42, 4422 (2017)
30fs is 10um
R. Wilcox, U.S. Patent 10,444,526

## Slide 38
According to theory, for small angles, dispersion and loss are low
Calculation/modeling of loss mechanisms
with angle
compensator
without angle
compensator
100fs pulses after
4:1 combination
Efficiency loss due to spatial dispersion:
Efficiency loss due to temporal dispersion:
combined beam

## Slide 39
Measured combining efficiency: 83.4%
Measured splitting efficiency (max combining efficiency): 84.7%
Dividing, we obtain 98% of theoretical efficiency
4:1 experiment: high efficiency, low dispersion
Phase stabilized by SPGD
120fs FWHM
Zhou et al, Opt. Lett. 42, 4422 (2017)

## Slide 40
Measured combining efficiency: 89.5%
Measured splitting efficiency (max combining efficiency): 90.7%
Dividing, we obtain 98% of theoretical efficiency
Phase stabilized by SPGD
120fs FWHM
8:1 experiment: high efficiency, low dispersion
Zhou et al, Opt. Lett. 43, 3269 (2018)

## Slide 41
power
amplifiers
l1
spatial
combiners
temporal
stackers
spectral
combiners
pulse compressor
stretchers and
pre-amplifiers
spectral
splitter
l2
l3
output
oscillator
…
Multidimensional coherent combination
Beam, pulse, and spectral combination
Achieves high energy, ultrafast pulses
High reprate and power, because fiber

## Slide 42
New laser will combine in space, time, spectrum
Block diagram
Schedule
Modulators
Amplifiers
Beam
combiners
Layout
Current funding ~$8M
Hardware designs
Lab space

## Slide 43
Recent experimental support
A
B
C
D
F
G
E
Bandwidth to support 50fs
3 spectral bands combine to 40fs pulse
Active and passive fiber drawn
for commercially produced fiber amp
SPECTRAL COMBINATION
TEMPORAL COMBINATION
Don Sipes, Optical Engines
Arto Nieminen, nLight
Siyun Chen, LBNL
Lauren Cooper, UM
AMPLIFICATION

## Slide 44
Conclusions and future work
We have stabilized large numbers of beams using advanced algorithms
This enables high-energy fiber laser designs
Ongoing work will make error correction faster
We are currently building a fiber laser with beam combination (27 beams), temporal combination (81 pulses), and spectral combination (3 bands)
  Target ~200mJ energy in ~40fs
  This will be a stepping stone toward high reprate accelerator drivers