## Slide 1: Thoughts on TPC Optimization
Xin Qian
BNL

## Slide 2: Outline
Detector Parameters
  TPC angle
  Wire pitch
  Wire angle
  Wire pattern
  Wire plane gap
Basic reconstruction
  Charge resolution
  Position resolution
  Image reconstruction quality
High level physics
  Particle identification
  Resolution

## Slide 3: Gain and Shaping Time Optimization for Cold Electronics

## Slide 4: Overview of Signal Processing
time
Number of ionized electrons
Signal on Wire Plane
Field Response
Signal to be digitized by ADC
Electronics Response
High-level tracking …
(Deconvolution)
V. Radeka
TPC signal consists of time and charge information from induction and collection planes
  Same amount charge was seen by all the wire planes

## Slide 5: Deconvolution
Fourier transformation
Time domain
Frequency domain
Back to time domain
Anti-Fourier transformation
Time Domain
Frequency Content
Deconvoluted Signals
The goal of deconvolution is to help extract charge and time information from TPC signals
Bruce Baller developed during Argoneut
Notes: Explain
1. What is filter like in the frequency domain?
2.Why filter is necessary (e.g. plot results w and w.o. filter )
3. Why we need a zero at zero frequency?

## Slide 6: Field and Electronics Response
Cold electronics:
4 shaping time (0.5, 1.0, 2.0, 3.0 us)
4 gain (4.7, 7.8, 14, 25 mV/fC)
Leon, SLAC
Charge vs. Time averaged for a single electron
Difference between simulation and data (bigger signal in LongBo arXiv:1504:00398)

## Slide 7: Discussion about Noise
There are two components of noise
  Electronic noise (ENC)
    The signal to noise ratio does not depend on the gain
    Longer shaping time has smaller noise
    Longer shaping time has slightly worse two-peak separation
  Digitization noise due to 12-bit ADC
    At 3 ms and 4.7 mV/fC, the electronic noise at collection plane is expected to be 0.58 ADC
    1/sqrt(12.) ~ 0.29 ADC
    11.7 ENOB  1.23/sqrt(12.) ~ 0.36
    12-bit ADC is enough so that “digitization noise” << “electronic noise”

## Slide 8: Discussion about Gain and Shaping Time
The choice of gain will not affect the signal to noise ratio
  Higher gain could lead to more chances of overflow
  Also need to take into account the zero-suppression algorithm
Longer shaping time would
  Increase the size of signal
    higher chance to overflow
  Reduce noise, thus increase signal/noise ratio
  Slightly worse two-peak separation (difference between 2.5 and 3 us)
  Also less digitization time (Nyquist: Tshaping >= 2 Tdigitization)
    Less data

## Slide 9: Optimization of Field Response Functions

## Slide 10: Gap between Wire Plane, Bias Voltage, and Grid Plane
The raw signal (digits) consists of both signal and (electronic) noise
  An ideal deconvolution will recover signal completely  number of electrons reached
  The deconvolution on the electronic noise will thus determine the signal to noise ratio
  Change in the gap distance and bias voltage will change  response function R  signal to noise ratio
  To be worked out

## Slide 11: MicroBooNE Case
In MicroBooNE, the second induction plane has the worst signal to noise ratio
Jyoti Joshi

## Slide 12: Some Questions
Preliminary results for 1D deconvolution
What’s the impact of dynamic induced charge?
  Data validation

## Slide 13: TPC Angle(I)
LArTPC
High density (Z ~ 18)
  Event are more compact
Parallel wire readout w.r.t. the beam direction
  More ambiguities
Slow detector response (~ms)
  Challenges in rejecting cosmics for detector on surface
Ultra-high resolution
  A layer ~ 3.5% X0 (14 cm R.L.)
Higher physics requirement
  ~ 80% efficiency
Liquid Scintillator
Low density (Z ~ 6)
Perpendicular wire readout w.r.t. the beam direction
Fast detector response (~10 ns)
High resolution
  A layer ~ 0.15 X0 (44 cm)
~35% efficiency in NOνA

## Slide 14: TPC Angle (II)
In a neutrino event, because of incident neutrino energy, the entire event is more boosted toward forward region
Due to nucleon response, the lepton tends to going more forward in the center-of-mass frame
TPC with wire readout has more trouble to reconstruct “tracks” which are parallel to the wire plane  charges arrive at various wire-plane at same time  ambiguity to figure out the proper correlation
http://www.phy.bnl.gov/wire-cell/ bee/set/4/event/2/

## Slide 15: Detector Angle
http://www.phy.bnl.gov/wire-cell/bee/set/7515fe16-d163-4df8-ad87-09f7c809dc7e/event/0/
Same events (rotate 0-19 degrees)
  Event 0  0 degrees
  Event 10  10 degrees
  Event 19  19 degrees

## Slide 16
0 degrees
10 degrees
One can click the web-site to look at events in 3D and rotate to get a better understanding.
10 degrees (truth)

## Slide 17
19 degrees
10 degrees
http://www.phy.bnl.gov/wire-cell/bee/set/6/event/8/
MC truth: one electron, one neutral pion, and one positve pion

## Slide 18: First Look at the TPC Orientation
Generated by GENIE
Look at the electron angle for two configurations: default vs. 10 degrees rotation
Integrated over all the energy, oscillation added
~ 20 % effect at the 0 degrees with rotating 10o
Effect is expected to be strongly energy-dependent
  Right plot shows the expected distribution at Argoneut (5-6 GeV) energy

## Slide 19: Questions
How to evaluate which angle is good enoug?
Is perpendicular wire-readout completely hopeless?
Can we add in intended distortion in electric field?
  How to calibrate its effect?

## Slide 20: Wire Pitch’s impact on Charge
For a electron drift at different locations within a wire pitch
  Field response has a strong dependence on the location of electron
Deconvolution was performed with average field response
Large wire pitch  smaller (electronic) noise to signal ratio  smaller resolution
Large wire pitch  larger spread at response function  larger resolution

## Slide 21: Questions
What’s the expected charge resolution and its dependence on the wire pitch?
How important is dynamic induced charge effect?
How to calibrate the 2D response function?

## Slide 22: About Wrapping (Wire Angle)
Wire angle would impact the wire wrapping scheme
What’s the problem of wire wrapping?
  The wrapping of wire would lead to more crossings of wires  the wires originally won’t cross can cross with wrapping  the crossing of wires will introduce ambiguities
True Hits
Fake Hits
u1
u2
v2
v3
At fixed time
v1
H1
H2
H3
H4
H5
H6
The amount of ambiguities strongly depends on the event activity
For a simple track, it is not a problem
For multiple tracks, more difficult
For showers, much more difficult
For shower + track + crossing APA  extremely difficult
Wire-cell imaging step is an ideal tool to study this (use both charge and time to do reconstruction)

## Slide 23: Wire Pitch/Angle on Position Resolution
Along the drift direction, the digitization length is 0.5 us * 1.6 mm/us  0.8 mm @ 500 V/cm
  Average diffusion σ=0.9 mm for 2.5 m drift distance
  Signal shaping time 2 us  2 us / 2.45 * 1.6 ~ σ=1.3 mm
For wire plane, the digitization length is related to the wire pitch (3 ~ 5 mm)
  For a continuous track, not a problem to calculate dE/dx
  For the end points of track, the resolution in “dx” is about “0.3 * L”
  Perpendicular to vertical wire: L = wire pitch
  Parallel to vertical wire: L ~ (wire pitch)/sin(theta)
  Consequences in short tracks (PID, angle, energy through range …)
  Gap identification (i.e. for e/gamma separation)
    Likely need “2 * L” to identify a gap
θ

## Slide 24: More about Gap Identification
Radiation length ~ 14 cm  for high-energy photon, the mean free path 9/7 * 14 ~ 18 cm
Assumption
  Along the drift direction: 4 us for two-peak separation
  Perpendicular to drift direction  2 * L
Observations:
3 mm 5 mm, gap identification efficiency is reduced by about 2.x% ~ (1-exp(-4/180))
~60% more background
36  45 degrees, the impact of gap identification efficiency is one order smaller
Also varied pitch for different planes (Maxim)

## Slide 25: Discussions
For bigger wire pitch, the gap identification efficiency will be reduced without a doubt
  3 mm  5 mm wire pitch leads to about 2.2 % reduction in efficiency
  But this number corresponds to ~60% more background
There are three weapons to differentiate electron from gamma:
  Gap identification
  dE/dx (initial track is about 3 cm long, what’s the impact of wire pitch?)
  Shower topology (i.e. gamma is always from neutral pion decay, thus multiple gammas)
The real question is “which wire pitch is good enough to reject background?”
Also engineering considerations
  Will small wire pitch leads to more chance of wire touching and high noise?

## Slide 26: These two would explain the shape of dE/dx plot
Compton Scattering
I calculated 5 cm mean free path based on moller scattering cross section, cross checked with MC

## Slide 27: e/gamma separation dE/dx
Compton ~ Z
Pair production ~ Z^2
Compton scattering could lead to confusion of dE/dx

## Slide 28: Summary
From reconstruction point of view, the priority (from high to low) is
  TPC angle (5-10 degrees from the beam direction)
    Within this range, larger angle is better
    When will be enough (i.e. increment is modest)?
  Wire Pitch (gap identification, dE/dx)
    3 mm is better
    Will 5 mm be enough?
  Wire Angle (reduce ambiguity, position resolution)
    To be studied
  Wire gap and bias voltage (charge resolution)
    To be studied