## Slide 1: Frequently Asked Questions
About LArTPC Reconstruction and Wire-Cell

## Slide 2
TPC reconstruction is not new. What's the main differences between gas TPC collider experiment and LArTPC neutrino experiment that cause extra difficulties?
  Why can they reconstruct thousands of tracks while you are struggling with reconstructing a few?

## Slide 3
  There are two main differences that makes event reconstruction in LArTPC neutrino experiment more difficult
    1. Event topology
    2. Wire vs. Pixel readout

## Slide 4
  Interaction (mainly) only happens at the colliding vertex
  Many auxiliary detectors (arranged typically in onion-shape)
    vertex detector, muon detector, TOF, EM/hadron calorimeter, etc.
  Magnetic field to help determine particle momentum and predict particle trajectory
  Association of tracks is relatively simple.
  Shower reconstruction is not as important
  Main challenge is the high multiplicity of tracks.
  Neutrino scattering can happen anywhere in the detector
  tracks and showers coming out at all directions.
    Both are our signals
  Secondary interactions are common due to high density
  Very few auxiliary detectors
  No magnetic field
  Correctly reconstructing and associating the tracks and showers are the main challenges in LArTPC.
Gas-TPC, Collider
LArTPC, Neutrino
    Event Topology

## Slide 5
  (continue)
  2. Wire vs. Pixel:
    Collider TPC typically use pad readout, which provide one 2-D image vs. time. A 3-D image can be directly obtained without ambiguity.
    In large LArTPC, driven by cost/power consideration, most experiments adopt wire readout, which provides only a few 1-D views vs. time. It is therefore a mathematically ill-posed reconstruction problem leading to degenerate solutions.
      The worst-case ambiguity is caused by parallel tracks: ionizing electrons from those tracks will arrive at the wire planes around the same time, causing many wires being hit simultaneously.
      The ambiguity is further amplified by the wrapping wires (e.g. in DUNE), where a single U or V wire views two opposite drift volumes.
      N^2 vs m*N
      (Hardware TPC optimization underway)

## Slide 6
What's the main differences between NOvA/MINERvA type detector and LArTPC?
Why are you still struggling with automated LArTPC reconstruction while they have already done full automated full-chain analysis with a much worse resolution detector?

## Slide 7
NOvA

## Slide 8
NOvA

## Slide 9
NOvA

## Slide 10
NOvA

## Slide 11
MINERvA

## Slide 12
MINERvA

## Slide 13
  ~40-60% efficiency probably OK
    The expected standard is much higher
      Superior resolution of the detector
      Must achieve >80% efficiency with high purity to reach physics goals in time
        Critical criteria when making technical decisions between WC and LArTPC
    Must do more than simple CCQE, CC-inclusive type analysis
      Basically want to reconstruct what we see.
      Intentionally smearing the fine image to use the existing reconstruction tools is possible but would only be a fallback/ complementary option.
        Won’t meet the expected performance
        Given the ambiguity of parallel tracks, the topology would still be different from NOvA/MINERvA even if we smear the image.
NOvA / MINERvA / MINOS
LArTPC
    Human Expectation

## Slide 14
  beam is near perpendicular to the view planes.
    The resulting lepton tracks are therefore mostly perpendicular to the view planes too.
    The hit multiplicity on each view plane is low and can be reconstructed with little ambiguity even without pad readout.
  beam is near parallel to the view planes
    Many tracks are therefore parallel to the view planes Both are our signals
    leading to large degeneracies due to the wire readout.
NOvA / MINERvA / MINOS
Most LArTPC
    Topology

## Slide 15
  Scintillator detectors, the timing scale is ~ns.
    The cosmic muon background rejection is therefore easier
  Scintillator signals directly tells the position of the tracks
  Electron drift time is slow ~ms.
    Need to be coupled with high efficiency scintillator detectors to efficiently reject cosmic muon background.
  Flash matching is needed to reconstruct the position of tracks from optical detectors and match the TPC measurements
NOvA / MINERvA / MINOS
LArTPC
    Timing

## Slide 16
  (continue)
  Hardware
    So far the quality of the electronics in LArTPC has not reached the level of those in scintillator detectors (NOvA/MINERvA) which typically have >99% good channels
    Maturity
    LArTPC is still a young technology and so is the reconstruction.

## Slide 17
Have you explored existing 3D pattern-recognition techniques to avoid re-inventing the wheels?
  Within HEP, there is no 3D pattern recognition exactly matching our needs due to the difficulties in topologies and ambiguities mentioned above. The solution space is large with many “corner cases”. More methods can be invented by human scanners on the fly.
    “No wheels exist yet”
  We are actively seeking and re-use concepts and codes where we can (e.g. Hough transformation, etc.). However there surely are still many methods that we are not aware of yet. We are eager to discuss the applicable ideas with experts from all fields.
  We are eager to collaborate with existing efforts (e.g. LArSoft, Pandora, etc.) to improve all areas of the reconstruction (clustering, fine tracking, PID, etc).

## Slide 18
I heard machine-learning/deep-learning can solve everything, why don't you go that direction?
  We are indeed exploring these fields. We need more experts to help us.
  We as physicists would like to better understand the problems first typically caused by underlining physics and detector properties, in order to provide better features to the different machine learnings.
    One of the ideas is to feed database of hand-scan operation/commands/solutions into the reinforcement learning. We would like to develop tools (e.g. Bee 2.0) to do that.
    Another idea is to feed raw waveforms to deep learning

## Slide 19
Why do you still advocate for hand-scan techniques in the modern era?
  Convenient hand-scan tools are important to ensure the correctness of the reconstruction.
    A 3-D hand-scan tool is required to fully understand the topology of the events.
  There are many "corner cases" where existing heuristics fail, but are likely to be identified by hand scan.
    Such scan results can be fed back to the reconstruction to improve the results.
    Such scan results also be fed back to machine for reinforcement learning.
  We are considering “semi-automated” hand-scanning:
    Automated high-signal-efficiency high-background-rejection pre-selection
    Hand-scan to improve the automated reconstruction efficiency and bias, and feed back to automated reconstruction
      We would like to develop tools (e.g. Bee 2.0) to do that
    Depending on the automated results, hand scan may be required in the end.

## Slide 20
What exactly are the CPU bottle-necks?
  Solving for “blobs” which attempts to remove a trial blob and re-compute the chi^2. This has explosive combinatorics. Current MCMC can still be slow depending on topology.
  Large number of channels -> N^2 number of cells
How to improve speed?
  Better algorithms
  Optimization
  Parallel
  GPU

## Slide 21
More Questions?
We would like to put these FAQs on our website so everyone can look and learn