## Slide 1: Beam-beam effects in KEKB/SuperKEKB
K. Ohmi (KEK)
Beam-beam workshop 2018@LBNL
5-7 Feb, 2018
Thanks to E. Forest, Y. Funakoshi, K. Hirosawa, N. Iida, H. Koiso, A. Morita,
Y. Ohnishi, N. Ohuchi, K. Oide, H. Sugimoto, Y. Zhang, D. Zhou

## Slide 2: KEKB
LER 3.5GeV(e+) x HER 8GeV(e-) asymmetric circular collider with circumf. 3016m.
L=2.16x1034 cm-2s-1 was achieved.
Overcome the Electron cloud effects.
Day-by-day tuning of coupling and its chromaticity.
SuperKEKB
LER 4GeV(e+) x HER 7GeV(e-) asymmetric circular collider (3016m).
Target L=8x1035 cm-2s-1.
Large crossing angle, szqh/sx=20, no crab waist.
Extremely low b*, bx*=3cm, by*=0.3mm. Low emittance.

## Slide 3: Parameters of KEKB/SuperKEKB
 | KEK (LER) | KEKB (HER) | SuperKEKB (LER) | SuperKEKB (HER)
ex(nm)/ ey (pm) | 18/180 | 24/240 | 3.2/8.64 | 4.6/11.5
bx/ by (mm) | 1200/6 | 1200/6 | 32/0.27 | 25/0.3
sz(mm)/sd(10-4) | 7/7 | 6/7 | 6/7.7 | 5/6.3
q(mrad), qP | 0.011, 1 | - | 0.0415, 20 | -
Ne | 6.4x1010 | 4.7x1010 | 9x1010 | 6.5x1010
Nbunch, tsp (ns) | 1576 | 1576 | 2500 | 2500
Ltot (cm-2s-1) | 2.11x1034 | - | 8x1035 | -
xx/ xy | 0.127/0.129 | 0.102/0.09 | 0.0028,0.088 | 0.0012/0.081

## Slide 4: Electron cloud cure and IP optics tuning
Chromatic coupling correction

## Slide 5: Commissioning of KEKB, IP optics tuning
IP orbit/optics tuning, Dx, Dy, ay, by (waist), r1-4, hy, hy’ every hour was essential for maintain KEKB operation.
Chromatic optics parameters, by, r1-4, hy. were corrected later.
Parametrization of one turn matrix at IP
  dispersion subtraction, 4+2 matrix
  x-y coupling

## Slide 6: Strong-strong simulation in SuperKEKB
Luminosity simulation was performed with scanning the optics parameters as is done in the operation. Simulation using M6(s*).

## Slide 7
Optics parameters are controlled by local bumps
Local bump at sextupole magnets induces x-y coupling at IP.

## Slide 8
Dispersion at IP, tuning
Beam size and luminosity are measured with changing hy parameters.

## Slide 9
X-y coupling LER R2 , tuning
Beam size and luminosity are measured with changing R2 parameters.

## Slide 10
X-y coupling LER R4 , tuning
Beam size and luminosity are measured with changing R4 parameters.

## Slide 11: Measurement of IP optics
Take turn-by-turn position data
Reconstruct phase space plot at IP.
Phase space ellipse
Octopos BPM
Octopos BPM
773mm
552mm
IPAC10

## Slide 14: Chromatic coupling at IP
Beam size blow-up was seen at nx-ny+-ns.
Existence of coupling term of xyz.
We correct chromatic coupling at IP using skew sextupole magnets.
Luminosity increases 20%, due to the crab cavity and chromatic coupling correction even lower beam current compare with the peak.

## Slide 15: Electron cloud cure and IP optics tuning
Chromatic coupling correction
Lower beam current

## Slide 16: Beam-beam simulation with chromatic coupling
Generating function of chromatic coupling transformation
en, fn,gn,hn are related to chromatic coupling.
Determine a-w for a given chromaticity (measurement or model)
Transfer using H(a,b,..)
…

## Slide 17: Weak-strong simulation w and w/o chromatic coupling
Specific luminosity w and w/o chromatic
coupling
Scanning dr4/dd and dr2/dd
D. Zhou et al., PRSTAB 13, 021001 (2010)

## Slide 18: Measurement of chromatic coupling
x-y coupling parameters are measured for RF freq shift.
Blue and red is before and after correction.
Luminosity increases 20% after the correction.
Y. Ohnishi et al., PRSTAB 12, 091002 (2009)

## Slide 19: SuperKEKB
Luminosity upgrade strategy changes the crab cavity to the large crossing angle scheme.
Extremely low b IP optics, bx*=3cm by*=0.3mm.
Large Piwinski angle,
Commissioning with collision starts from this spring.
IP beta is squeezed step by step,
(8xbx*,8xby*), (4xbx*,8xby*), (4xbx*,4xby*),…, (bx*,by*)
Two subjects are discussed,
IR nonlinearity
Coherent beam-beam instability

## Slide 20
Y. Ohnishi, Dec. 2017

## Slide 21: IR magnets and their nonlinearity
There are many nonlinear field components in IR magnets.
Chromatic coupling
D. Zhou, SKEKB MAC 2015
BBWS : arc expressed by simple transfer matrix
SAD: complex lattice structure

## Slide 22: Y. Zhang’s (IHEP) work at KEK
Vertical orbit is induced by a large horizontal betatron oscillation.
Skew sextupole term at IP, x2y, is suspected for the luminosity degradation.

## Slide 23: QCS superconducting magnet system
N. Ohuchi et al.

## Slide 24
N. Ohuchi et al.

## Slide 25: Evaluation of nonlinear term
Focus on skew sextupole component.
Reference axes in solenoid is chosen as a straight line with half crossing angle.
Magnet components are defined on the reference orbit.
Beam orbit deviate from the reference orbit.
Skew sextupole component is induced by Skew sextupole and octupole with a vertical orbit.
Skew sextupole component
upstream of IP downstream

## Slide 26: C10 from SK2 and K3+yCOD
Contribution to SK2 is coming from explicit Skew Sext SK20 and octupole, K3+COD
No contribution from higher order than K3.
Skew sextupole coming from higher order nonlinearity is small.
There are 10 skew components.

## Slide 27: Comparison with PTC
D. Zhou

## Slide 28: Luminosity for H=c10px2py
The luminosity degradation due to c10 is weaker than that of beam-beam simulation with SAD.
There may be still unknown nonlinearity?

## Slide 29: Detuning b*
  c10=0.072 m is kept for b*change, because IR magnets are fixed in SuperKEKB.
  For normalized coordinates, ,
  C10=136.9 m-1/2 for bx*=3.2cm, by*=0.27mm
  Normalized C10 directly affects the beam dynamics.
  The effect is reduced by Detune of b*.
  C10 is 4.4% for 8x8, 8.8% for 4x8.
for bx*=3.2cm, by*=0.27mm

## Slide 30: Measurement of the Coherent beam-beam instability
Beam-beam instability should be observed at detuned lattice (8x8x) in commissioning of Phase-II (this year).
Design parameters of SuperKEKB was stable.
Y. Ohnishi, Dec. 2017

## Slide 31: Analysis of the instability
Beam-beam eigenmode analysis. Solve eigenvalues of 1000x1000 matrix.
Eigen tune is n=nx+-Lns. Mode coupling or synchro-beta resonance is casued.
Synchrotron tune, ns(LER)=0.0247, ns(HER)=0.0280.
Number of Sidebands increases. More unstable.
strong-strong beam-beam
simulation.

## Slide 32: Eigen mode analysis for nx=0.53
8x8x 4x8x
skb8x8xb
nx+ns(+)
nx-3ns(-)

## Slide 33: Eigen mode analysis for nx=0.54
8x8x 4x8x
skb8x8xc

## Slide 34: Eigen mode analysis for nx=0.55
skb8x8xd
8x8x 4x8x

## Slide 35: Strong-strong beam-beam simulation 8x8x, 1.44mAx1.04mA, nx=0.53
skb2a

## Slide 36: 4x8x, 1mAx0.8mA , nx=0.53
skb21b

## Slide 37: Summary of the strong-strong simulation
nx | 8x8x L/L0, sx/sx0 (L & H) osc. | 4x8x L/L0, sx/sx0 (L & H) osc.
0.53 a | 0.58-0.66 6.5 4.5 | 0.75-1.0 3.0-7.5 2.2-6.2
0.535 g | 0.70-0.95 2.5-6.2 1.4-4.0 | 1.04 1.2 1.0
0.54 d | 0.75-0.95 2.5-6.0 1.4-4.0 | 1.05 2.1 1.1
0.545 f | 0.83 7.2 1.2 no osc. | 0.94 5.2 1.7
0.55 e |  | 0.75-0.77 8.6 3.5
I=1.44mA x 1.04mA
Horizontal emittance growth does not contribute luminosity drop in collision with a large crossing angle, when by is large.
Crab waist on in the simulation. CW-off may be serious for the horizontal emittance growth.

## Slide 38: Summary
SuperKEKB collision starts this spring (Phase II).
Beta function is squeezed step-by-step.
From the beam dynamics, these two issues are
  1. IR nonlinearity
  2. Coherent beam-beam in head-tail mode
Also studies to be continued
  3. Electron cloud/ion
  4. IR linear optics

## Slide 39: Thank you for your attention

## Slide 40: Commissioning of KEKB
Electron cloud effect, this is not subject of this work shop.
IP orbit/optics tuning, Dx, Dy, ay, by (waist), r1-4, hy, hy’.
Chromatic optics parameters, by, r1-4, hy.
Parametrization of one turn matrix at IP