## Slide 1: Achromatic Telescopic Squeezing (ATS) scheme in the context of long-range beam-beam compensation techniques
S. Fartoukh, CERN, Beams Department
with contributions from several LHC teams: Operation,
Optics-Measurement-and-Correction, Collimation, Lumi, Beam-beam ..
Beam-beam Workshop 2018

## Slide 2: Contents
ATS motivations and basic principles
Effective construction of ATS optics and summary of by-products
BBLR mitigation with octupoles for telescopic optics with highlights from MD
BBLR compensation with wires with emphasize on flat optics
Summary and outlook

## Slide 3: ATS Motivations
Lower b* need magnets of larger aperture, and new HW or sophistication (crab-cavity, flat optics) to “profit from the low b*”.
the HL-LHC Project
But this does not tell how to produce the b*
 the ATS scheme (PRSTAB 18-111002, 2013) which solves many optics limitations coming from the overall ring:
1. Optics matchability to the arcs:
  Some IR quads going to 0 T/m, others to max. field (200T/m)
  Simply the matching section becomes too short at some point!
  2. Correctability of the chromatic aberrations induced, not only Q’, but also Q’’, Q’’’,…, and off-momentum b-beating.
   Arc sextupole strength (<600A)

## Slide 4: Basic principles
How: a squeeze in two steps
1. The Pre-squeeze:
An “almost” standard squeeze,
 acting on the matching quads of IR1 and IR5 with new matching constraints on the left/right IR phase,
 till reaching some limits on matching quads (or sextupoles)
The Tele-Squeeze:
A further reduction of b*,
 Acting only on IR2/8 for squeezing IR1 and IR4/6 for IR5,
 Inducing b-beating bumps in s81/12/45/56 to boost the sextupole efficiency, but also the octupoles (see later).

## Slide 5
b*= 40 cm
Un-precedent b* w/o chromatic limit (see later) can now be reached based on a kind of generalized squeeze involving 50% of the ring
b*= 10 cm
Beam sizes [mm] @ 7 TeV from IR8 to IR2 for typical ATS “pre-squeezed” optics (left) and “telescopic” collision optics (right)
The new IR is sort of 8 km long !

## Slide 6
First demonstration with beam in 2011 (.. already with 30 cm b* !)
 Telescopic principle (×4) demonstrated in IR1
Thanks to G. Vanbavinckhove & OMC team

## Slide 7
The magic lies in the choice of the betatron phases
Zoom in arc45: Pre-Squeeze to b*=40/40 cm (round optics)
Dmy  p between strong SD’s (every other FODO cells)
Dmy (Q11 IP ) = 1.25×p + ey
with ey ~ 1/2 tan-1 (bmin/bmax)
(barc× b*)V  cst
Dmx  p between strong SF’s
(every other FODOcells)
Dmx(Q10 IP ) = 0.75×p + ex
with ex ~ - 1/2 tan-1 (bmin/bmax)
 (barc× b*)H  cst
IR4
(RF insertion)
IR5
(CMS insertion)
p/2 phase in the arc cells
2 sextupole families per plane but
only one used for triplet correction
 p/2 on the left/right side of the IR
Effective Construction

## Slide 8
Zoom in arc45: Squeeze to b*=10/10 cm (round optics)
 Tele index of 4H×4V
Dmy  p between strong SD’s (every other FODO cells)
Dmy (Q11 IP ) = 1.25×p + ey
with ey ~ 1/2 tan-1 (bmin/bmax)
(barc× b*)V  cst
Dmx  p between strong SF’s
(every other FODOcells)
Dmx(Q10 IP ) = 0.75×p + ex
with ex ~ - 1/2 tan-1 (bmin/bmax)
 (barc× b*)H  cst
IR4
(RF insertion)
IR5
(CMS insertion)

## Slide 9
Dmy  p between strong SD’s (every other FODO cells)
Dmy (Q11 IP ) = 1.25×p + ey
with ey ~ 1/2 tan-1 (bmin/bmax)
(barc× b*)V  cst
Dmx  p between strong SF’s
(every other FODOcells)
Dmx(Q10 IP ) = 0.75×p + ex
with ex ~ - 1/2 tan-1 (bmin/bmax)
 (barc× b*)H  cst
IR4
(RF insertion)
IR5
(CMS insertion)
Zoom in arc45: Squeeze to b*=20/5 cm (flat optics)
 Tele index of 2H×8V

## Slide 10
The by-products comes from the (controlled) b-beating induced in the IR1/5 adjacent arcs, and from the phasing of these arcs w.r.t the triplet.
  Q’ correction at constant sextupole strength:
   no b* limits from Q’ correct-ability
  Very clean compensation of chromatic aberrations, such as off-momentum b- beating, non-linear chromaticity, spurious dispersion from crossing angle
     preservation of off-momentum triplet aperture, IR7 hierarchy preservation over the RF bucket (no degradation of TCP/TCS retraction), control of chromatic tune spread (Q”, Q’’’,..), other exotic effects avoided like strong pacman effect on Q’
  Lattice octupoles (MO) boosted at cst strength:
     More Landau damping to cope with impedance/intensity increase,
     Using the octupoles in SB for BBLR mitigation  X-angle reach
By-products (a summary)

## Slide 11
.. Some illustration: Chromatic corrections (Q’): No b* limits
Only 25% of the RS circuits participates to the chromatic correction during the pre-squeeze
b*: 40 cm  10 cm
During the telescopic part, the chromatic correction is achieved by the b-beating!
b*> 40 cm
Typical sextupole settings [A] for the 32 families available per beam (from MD in 2011 @ 3.5 TeV)
 All sextupole then kept ~ constant during the tele-squeeze

## Slide 12: b’s at the MO’s vs. telescopic index
Telescopic squeeze
(× 4x, × 4y)
Strong OD
Strong OF
Weak OF
Weak OD
BBLR mitigation with octupoles
 Two categories of octupoles in s81/12/45/56: the “strong” (with increased ) and the “weak” (with decreased )
Beam 1/2 | “Strong“ OF.b1/OD.b2 | Weak OF.b1/OD.b2 | Strong OD.b1/OF.b2 | Weak OD.b1/OF.b2
Sector 45 (81) | 22.R4(8), 26.R4(8), 30.R4(8), 34.R4(8), 30.L5(1), 26.L5(1), 22.L5(1) | 24.R4(8), 28.R4(8), 32.R4(8), 32.L5(1), 28.L5(1), 24.L5(1) | 25.R4(8), 29.R4(8), 33.R4(8), 31.L5(1) | 31.R4(8), 33.L5(1), 29.L5(1), 25.L5(1)
Sector 56 (12) | 31.R5(1), 33.L6(2), 29.L6(2), 25.L6(2) | 25.R5(1), 29.R5(1), 33.R5(1), 31.L6(2) | 22.R5(1), 26.R5(1), 30.R5(1), 34.R5(1), 30.L6(2), 26.L6(2), 22.L6(2) | 24.R5(1), 28.R5(1), 32.R5(1), 32.L6(2), 28.L6(2), 24.L6(2)
Total | 7+4 = 11 | 6+4 =10 | 4+7 =11 | 4+6=10

## Slide 13: Phases at the MO’s vs. telescopic index
 A clean mitigation of the BBLR effects is a priori within reach for both the octupole tune spread and the (4,0), (0,4) and (2,±2) driving terms
 p/2 + e
 p/2 - e
As for the strong sextupoles (participating to the IT chromatic correction), all the strong OF (resp. OD) are located at an H phase (resp. V phase) very close to p/2+ kp w.r.t. the IP, so p w.r.t. the triplet and the LR beam-beam encounters.
Telescopic squeeze
(× 4x, × 4y)

## Slide 14: Guidance from simulations for MD preparation
Tele-index rtele
MO tune spread amplification at
constant strength during the Tele-Squeeze
> 400% for a tele-index of 4
(typical HL-LHC)
~ 60 % for a tele-index of 2
(very reasonable for LHC)
At large tele-index (>3), the MO’s are so efficient that they can mitigate
the long-range Beam-Beam effect
Simulated MO scan with 150 mrad X-angle
Nb=1.2E11, ge=2.5 mm, and rtele ~ 3 (from 1 m to 35 cm)
DQspread

## Slide 15
 Significant reduction of the crossing angle going from positive to negative octupole polarity.
Thanks to D. Pellegrini
MD Optics choice: tele-index of 3
(stopping the pre-squeeze @ 1 m, and reaching b*=35 cm telescopically)

## Slide 16
MD results
 Preparation and validation for high intensity of this special telescopic optics to reach this beautiful result in the end of 2017 !
Courtesy of A. Poyet, G. Sterbini, and LHC Beam-Beam team
Burn-off limit
@ 80 mb

## Slide 17
Zoom
 X-angle reach: starting with MO<0 in another fill, the life time improved by reducing the X-angle ! Up to 20 mrad (10%) could be gained in X-angle
Courtesy of A. Poyet, G. Sterbini, and LHC Beam-Beam team

## Slide 18
Motivation: Flat optics (not flat beams!) means
.. with the crossing plane corresponding to the plane of largest b* (i.e. smallest b in the triplet).
  To preserve/gain aperture in the triplet (smaller X-angle requested)
  To maximize the luminosity via a mitigation of the geometric loss factor
Luminosity calculated for head-on colliding round beams
r.m.s. bunch length (7.5 cm nominally but 9-10 cm in practice for various reasons)
Full normalized X-angle (9-10 s for LHC, up to 12.5 s for HL-LHC with more current and longer triplet with more LR’s )
Flat optics and wire compensation
Increasing the b* aspect ratio could in principle rapidly mitigate the geometric luminosity loss w/o need of crab-cavities.
But w/o dedicated action, the normalized X-angle should unfortunately increase as well together with the b* aspect ratio …

## Slide 19
Flat optics example: HL-LHC plan B for 1035 virtual luminosity w/o crab-cavities but BBLR wire (PRSTAB 18-121001, 2015)
 b*=40/10 cm at IP1&5 (i.e. r=4), Qc=300 mrad, i.e. about halved vs. baseline but still 10.5 s at b*=40 cm in the X-plane, ho collision at full current in 3 IPs
A ``monster’’ before correction (DQho=0.025, DQLR=0.015)
 Contrary to round optics, no self-compensation between IR1 and IR5 for b2 (tune shift), b6 (“wings”), b10 …
A regular HO footprint after correction (DQho=0.025, DQLR=0.0)
with wire installed at optimal position (see later)
Courtesy of S. Valishev and D. Shatilov

## Slide 20
The “magic” of the BBLR compensation with wires.. that “simple mitigation” with octupoles cannot provide
R ~ 2
R ~ 1/2
The choice of b aspect ratio at the wires is crucial.
bx/by = 1 is a very poor compromise with only 1 wire/IR (although thought optimal for many years).
With 2 wires/IR, symmetric left/right @ bx/by ~ 2 and ½ (thank to the LHC-like optics anti-symmetry), the compensation is optimal for all driving terms (see details in PRSTAB 18-121001, 2015)!
With LR encounters taking place at non uniform normalized beam-beam separation, can we compensate all RDT’s with only 1 or 2 wires?
If yes, can we build an automatic tool for setting generation (transverse wire position and current) working for arbitrary optics (flat or round) and crossing angle ?
Are there any preferences (based on beam dynamics criteria) where to install the wire, i.e. at which b-function aspect ratio ? Is an aspect ratio of 1 really the optimal choice?
Normalized beam-beam separation at LR encounters
for typical LHC collision optics

## Slide 21
Assuming two wires/IR and with optics anti-symmetry, a priori only 2 (+2) RDTs can be corrected.
But actually much more can be achieved by a proper choice of the b aspect ratio at the wire.
From 1rst to 3rd order
From 4th to 8th order
From 9th to 10th order
Correction (04)-(40)-(60)-(06)
Regardless of the correction type all the RDTs are vanishing at
rw ~ 2 and rw ~1/2
Correction (04)-(40)-(28)-(82)
Correction (22)-(55)

## Slide 22
Machine Development at the LHC:
Pre-squeezed stopped at 60/60 cm followed
by two tele-squeeze segments
To reach 60/15 cm at IP1 and 15/60 at IP5
Then 30/12 cm at IP1 and 12/30 cm at IP5
Optics measurement and correction at (60/15)-(15/60)
 20% level in H and 10% level in V !
Courtesy of T. Persson and OMC team
 First flat optics MD took place end of the 2017 with small intensity beams, for optics measurements and correction, with already very encouraging results.

## Slide 23
More to come in 2018: X-angle reach with flat optics ??
 In the range of 12-13 s for a b* aspect ratio of 4 and for LHC type beams (up to 15 s for HL-LHC beams), compared to ~9 s in LHC for round optics (self-compensation of the BBLR spread between IR1 and IR5 for round optics)
 Is the mitigation with octupole enough to reach the 10 s level for flat optics, or will we effectively need the wires??
(60/15)-(15/65) flat optics @ 150 mrad
 12.2 s @ ge=2.5 mm and 6.5 TeV
Note DQLR ~ - 0.007 along the diagonal
(60/15)-(15/65) flat optics @ 125 mrad
 10 s @ ge=2.5 mm and 6.5 TeV
Note DQLR ~ - 0.010 along the diagonal
DQ=0.025
DQ=0.025
The MO are still very efficient on the BBLR spread but not on tune shift (typically DQLR ~ - 0.01 along the diagonal @ 1.25E11 /bunch), which is also changing from bunch to bunch (pacman effect)
Also, the footprint wings (b6-like effects) are left uncorrected !

## Slide 24
Preliminary results with LHC flat optics (60/15)
(full study done by N. Karastathis)
WP optimization
@ MO=0 and 1.25E11
Octupole to - 550A
(only small gain)
X-angle reach vs. intensity
with new WP and MO@-550A
150 mrad (12.2 s)
challenging @ 1.25E11 !
125 mrad (10.0 s)
should be easy @ 1.25E11 !
(.31/.32)
Pacman bunches remains to be checked

## Slide 25: Summary
The ATS scheme is not only the key for low b* collision optics at the (HL-)LHC, but it also opens a new world of applications, in particular:
The possible mitigation of the BBLR effects with the arc Landau octupoles and therefore some reduction of the X-angle and gain in performance  LHC Run III
The feasibility of flat optics with even smaller b* in one of the two transverse planes, which a priori needs the cleanest possible BBLR compensation (wires, TBC) to fully exploit their potential  HL-LHC Plan B

## Slide 26: Spare

## Slide 27
2016
(150 mrad @ b*=40 cm)
2017
(with X-angle levelling: 150 120 mrad)
Beam 1
Beam 2
Beam 1
Beam 2
Beam Stabilization @ ~2.3h
Beam Stabilization @ ~1.6h
Life time: effective cross section in Stable Beam (all fills)
X-angle steps
Further X-step tried out for a couple of fills only
Courtesy of G. Iadarola, N. Karastathis
and Lumi team

## Slide 28: X-angle steps in 2017
Courtesy of N. Karastathis and Lumi team