## Slide 1
Beam-beam modelling revision in SIXTRACK
G. Iadarola with input from:
J. Barranco, X. Buffat, R. De Maria, S. Furuseth, N. Karastathis,
Y. Papaphilippou, D. Pellegrini, K. Sjobaek
Workshop on Beam-beam effects in Circular Colliders
Berkeley 5-7 Feb 2018

## Slide 2
Outline
Introduction
  SixTrack
  Beam-beam effects in SixTrack
  Review of the 6D beam-beam routines
Numerical model
  Transverse generalized kicks
  Linear coupling treatment
  Energy change
Performed tests
  Overview
  Boost/anti-boost
  Linear coupling
What next

## Slide 3
Outline
Introduction
  SixTrack
  Beam-beam effects in SixTrack
  Review of the 6D beam-beam routines
Numerical model
  Transverse generalized kicks
  Linear coupling treatment
  Energy change
Performed tests
  Overview
  Boost/anti-boost
  Linear coupling
What next

## Slide 4
SixTrack
SixTrack is CERN’s workhorse for tracking studies in high energy rings (e.g. LHC, HL-LHC, FCC), extensively used for:
  Dynamic Aperture studies (evaluating the effect of magnetic imperfections and beam-beam)
  Collimation studies (loss maps, collimation efficiency, background at the experiments)
  Study of failure scenarios (e.g. for crab cavities)
It supports Linux, Windows, MAC in a numerically portable way
It is integrated in the LHC@Home volunteer computing platform, based on BOINC (bits of tracking studies performed by volunteers on their pc)
http://sixtrack.web.cern.ch/SixTrack/
http://lhcathome.web.cern.ch
http://boinc.berkeley.edu

## Slide 5
Beam-beam in SixTrack
In the past the optics of the strong beam was computed from the optics of the weak beam assuming an anti-symmetry conditions
An expert mode was recently introduced to have fully independent optics and closed orbit of the strong beam. Necessary for LHC and HL-LHC studies involving flat optics and/or crab cavities (details here)
Beam beam effects are simulated using the weak-strong approach
The typical simulation includes both head-on and long-range beam-beam encounters:
  Long-range encounters are modeled with 4D beam-beam lenses (Bassetti-Erskine, only transverse kicks)
  Head-on encounters are simulated using the “6D” modeling based on Hirata’s “Synchro-beam mapping”  main topic of this talk
The effect of linear coupling of the strong beam can be taken into account in the simulation (never really tested/used)
Example LHC DA study
N. Karastathis

## Slide 6
Review of the 6D beam-beam routines
[1] A symplectic beam-beam interaction with energy change, by K. Hirata, H. W. Moshammer, F. Ruggiero, 1992
[2] Don't be afraid of beam-beam interactions with a large crossing angle, by K. Hirata, 1993
[3] 6D Beam-Beam Kick including Coupled Motion, by L.H.A. Leunissen, F. Schmidt, G. Ripken, 2001
[4] 6D beam-beam interaction step-by-step, G. Iadarola, R. De Maria, Y. Papaphilippou
Implementation based on Hirata’s BBC code [1,2], later extended by Leunissen, Schmidt and Ripken [3] to include the effect of linear coupling of the strong beam
Active work on core beam-beam routines stopped in the early 2000’s, and slowly the knowledge on the implementation details got a bit “forgotten”
  code review activity recently launched, driven by needs of the HL-LHC upgrade
Code structure and interface documented in SixTrack Wiki (mainly by J. Barranco)
Invested some time in understanding and re-constructing the mathematical treatment trying to use as little as possible the source code as a reference
  Parts not available in literature were re-derived (mainly inverse Lorentz boost, and a large fraction of the coupling treatment)  prepared a document including the full set of equations [4]

## Slide 7
Outline
Introduction
  SixTrack
  Beam-beam effects in SixTrack
  Review of the 6D beam-beam routines
Numerical model
  Transverse generalized kicks
  Linear coupling treatment
  Energy change
Performed tests
  Overview
  Boost/anti-boost
  Linear coupling
What next

## Slide 8
A dance of reference systems
s
x
y
Weak beam
Strong beam
Crossing plane
a
2f
We assume that we are in the reference system of the weak beam
The Interaction Point (IP) is at s=0
The crossing plane is defined by our s-axis and by the strong beam
We call a the angle between the crossing plane and the x-s plane
We call f the half crossing angle

## Slide 9
Weak beam
Strong beam
Barycentric reference frame
IP
Crossing plane
We look at the problem in the crossing plane
We introduce the “barycentric” reference system in which the weak and the strong beam are at +f and -f respectively
f
A dance of reference systems

## Slide 10
Weak beam
Strong beam
Barycentric reference frame
S
IP
Crossing plane
In the crossing plane the interaction looks like this…
To apply the Hirata, Moshammer, Ruggiero treatment we practically need to suppress the angle for the two beams (impossible by simple rotation)
A dance of reference systems

## Slide 11
Weak beam
Strong beam
Barycentric reference frame
Boosted
reference frame
S*
S
IP
Crossing plane
In the crossing plane the interaction looks like this…
To apply the Hirata, Moshammer, Ruggiero treatment we practically need to suppress the angle for the two beams (impossible by simple rotation)
This can be achieved by using a boosted frame that is moving w.r.t. the lab
A dance of reference systems

## Slide 12
IP
Boosted
reference frame
S*
Weak beam
Strong beam
Crossing plane
In the boosted frame the interaction looks like this
A dance of reference systems

## Slide 13
IP
Boosted
reference frame
S*
Weak beam
Strong beam
Crossing plane
The strong beam is cut in several slices having different transverse offset
The synchro-beam method: transverse “generalized kicks”

## Slide 14
Boosted
reference frame
S*
IP
z=0
z=0
Crossing plane
A particle with z=0 and a slice having z=0 collide at the IP
The synchro-beam method: transverse “generalized kicks”

## Slide 15
Boosted
reference frame
S*
Crossing plane
IP
z=0
z>0
z=0
Collision Point
(CP)
A particle and a slice with generic z coordinates will collide at a different s coordinate, Collision Point - CP, given by:
(in sixtrack jargon z is called s)
The synchro-beam method: transverse “generalized kicks”

## Slide 16
We proceed as follows:
We drift the slice and the weak particle from the IP to the CP
Boosted
reference frame
S*
Crossing plane
IP
z=0
z>0
px>0
z=0
Collision Point
(CP)
(a particle and having an angle will probe the strong-beam electric field at a different transverse coordinates)
w.r.t. the slice centroid
We apply the kick a the CP:
We drift the particles back from the CP to the IP using the new angles:
Transverse kicks need to be computed based on the shape of the strong beam…
The synchro-beam method: transverse “generalized kicks”

## Slide 17
Optics of the strong beam: S matrix
The shape of the strong beam is described by 4D correlation matrix (S-matrix)
Convention:
1x, 2px, 3y, 4py
Points having same phase space density lie on hyper-elliptic manifolds defined by the equation:
The phase space distribution can be written as:
S contains all the information about the beam shape and divergence (including linear coupling) and can be transported from the IP to the CP (assuming that we are in a drift):
with

## Slide 18
Transverse kicks - linear coupling of the strong beam
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate

## Slide 19
Transverse kicks - linear coupling of the strong beam
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate

## Slide 20
Transverse kicks - linear coupling of the strong beam
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate

## Slide 21
Transverse kicks - linear coupling of the strong beam
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate

## Slide 22
Transverse kicks - linear coupling of the strong beam
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate

## Slide 23
Transverse kicks - linear coupling of the strong beam
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate

## Slide 24
Transverse kicks - linear coupling of the strong beam
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate

## Slide 25
Transverse kicks - linear coupling of the strong beam
q
Semi-axes in the decoupled frame:
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate
Coupling angle and beam sizes in the de-coupled frame need to be evaluated:

## Slide 26
Transverse kicks - linear coupling of the strong beam
q
In general, linear coupling of the strong beam can be present:
The coupling angle and the beam sizes in the decoupled frame can be obtained by diagonalization of the S-matrix
Coupling angle depends on the s-coordinate
Coupling angle and beam sizes in the de-coupled frame need to be evaluated:

## Slide 27
q
Once the coupling angle and the beam sizes in the decoupled plain are known, we proceed as follows:
We calculate the particle coordinates in the decoupled frame at the CP:
We calculate the kick from the slide in the decoupled reference frame:
where
is the electric potential
For Gaussian (uncoupled) beams, closed forms exist to evaluate these quantities.
Bassetti-Erskine
Transverse kicks - linear coupling of the strong beam

## Slide 28
q
Once the coupling angle and the beam sizes in the decoupled plain are known, we proceed as follows:
We calculate the particle coordinates in the decoupled frame at the CP:
We rotate the kicks to de coupled reference frame
We apply the kicks to the transverse momenta and drift back to the IP (as explained before)
We calculate the kick from the slide in the decoupled reference frame:
where
is the electric potential
For Gaussian (uncoupled) beams, closed forms exist to evaluate these quantities.
This map by itself is not symplectic  it becomes symplectic when longitudinal forces are also included [1]…
Transverse kicks - linear coupling of the strong beam

## Slide 29
Boosted
reference frame
S*
Energy change: effect of the angle
IP
z>0
px>0
Collision Point
(CP)
v
Estrong
The longitudinal kick has two components:
The trajectory is, in general, not perpendicular to the transverse fields of the strong beam  this introduces this term in the longitudinal kick (see Hirata [1] for detailed explanation)

## Slide 30
Energy change: grad-phi effect
Another component of the longitudinal kick arises from the fact that the transverse shape of the strong beam is changing along z (hour-glass effect, “rotating” coupling angle)
  The electric potential depends on z
  The gradient of the electric potential (i.e. the electric field) has a z component
  There is a z-kick, i.e. again a change in the particle energy
We need to evaluate the derivative w.r.t. z of the electric potential
As we have written down most of the involved quantities as a function of the coordinate of the CP (capital-S) we just notice that:
The longitudinal kick has two components:
(in sixtrack jargon
z is called s)

## Slide 31
Energy change: grad-phi effect
where:
Derivative rule for nested functions:
We need to evaluate these eight terms…

## Slide 32
Energy change: grad-phi effect
For these four terms a closed forms exist for transverse Gaussian beams
Bassetti-Erskine

## Slide 33
Energy change: grad-phi effect
With some some goniometric trick
Where:
Terms coming from linear coupling

## Slide 34
Energy change: grad-phi effect
Derivatives of R, T and W
Terms coming from hourglass effect

## Slide 35
Handling the denominators
We have all the pieces, but on the way we introduced some denominators which can become zero!  not handled in SixTrack, properly treated in [4]

## Slide 36
Outline
Introduction
  SixTrack
  Beam-beam effects in SixTrack
  Review of the 6D beam-beam routines
Numerical model
  Transverse generalized kicks
  Linear coupling treatment
  Energy change
Performed tests
  Overview
  Boost/anti-boost
  Linear coupling
What next

## Slide 37
Very difficult to identify problems by using the full tracking simulations
  Need to test the single routine “on the bench”
Procedure performed for each functional block:
  Built a C/python implementation from the equations in the document [5]
  Extracted the corresponding sixtrack source code and compiled as of a stand-alone python module (f2py)
  “Stress test” performed on the two: consistency checks, comparison against each other
Validation tests

## Slide 38
Validation tests
Part of the code | Tests performed | Outcome
Boost/anti-boost | Comparison Sixtrack vs C/python routine Checked that the two cancel each other | Bug identified and corrected
Beam-beam forces (with potential derivatives w.r.t. sigmas) | Comparison sixtrack vs C/python routine Force compared against Finite Difference Poisson solver (PyPIC) Other derivatives compared against numerical integration/derivation | All checks passed
Beam shape propagation and coupling treatment | Comparison Sixtrack vs C/python routine Comparison against MAD for a coupled beam line Crosscheck with numerical derivation | Bug identified and corrected Vanishing denominators not treated correctly  correct treatment developed and implemented in the library, to be ported in SixTrack
Slicing | Check against independent implementation | Passed but precision is quite poor (1e-3)
Computation of the kicks | Check against independent implementation | All checks passed
In the following I comment only on these two parts…

## Slide 39
TRACK(2)=(TRACK(2)+CALPHA*SPHI*H1)*CPHI
TRACK(4)=(TRACK(4)+SALPHA*SPHI*H1)*CPHI
TRACK(2)=(TRACK(2)*CPHI+CALPHA*TPHI*H1)
TRACK(4)=(TRACK(4)*CPHI+SALPHA*TPHI*H1)
Digging a bit we found out that the issue was already present in BBC (1996), on which the Sixtrack implementation is based, and quietly survived for >20 years
Boost/anti-boost
SixTrack routine
x 6.5e-19
px 0.065
y 4.3e-19
py 0.027
sigma 0.0
delta 2.0e-17
Python test module
x 4.3e-19
px 0.0
y 4.3e-19
py 3.e3-17
sigma 0.0
delta 1e-16
Error after boost + anti-boost (example)
SixTrack corrected
x 6.5e-19
px 5.55e-17
y 4.3e-19
py 0.1e-19
sigma 0.0
delta 2.0e-17
Discrepancy found between in the anti-boost between derived equations and SixTrack source code:
Boost and anti-boost should cancel each other exactly
  Problem identified in the Sixtrack implementation

## Slide 40
Impact on realistic simulation study assessed by D. Pellegrini
Tune scans comparison with 2017 ATS optics show no dramatic change, but slightly worse DA
Old version
Corrected version
Boost/anti-boost

## Slide 41
Skew
quadrupole
S-matrix propagation with linear coupling
Library tested against MAD-X:
Built a simple line with a strong skew quadrupole
Entering with a de-coupled beam
Saves S-matrix at regularly spaced markers for comparison
Skew
quadrupole
Dots: MAD-X
Lines: SixTrack

## Slide 42
S-matrix transformation to un-coupled frame
Verified against numerical diagonalization of the S-matrix:
Sign error in the computation of the coupling angle
Coupling angle [deg]
if(abs(sinth).gt.pieni) then
sinth=(-1d0*sfac)*sqrt(sinth)
else
sinth=zero
endif
Original source code:

## Slide 43
Coupling angle [deg]
S-matrix transformation to un-coupled frame
Verified against numerical diagonalization of the S-matrix:
Sign error in the computation of the coupling angle
if(abs(sinth).gt.pieni) then
sinth=(sfac)*sqrt(sinth)
else
sinth=zero
endif
Corrected source code:

## Slide 44
{'Sig_11_0': 2.1046670129999999e-05, 'Sig_12_0': 2.7725426699999999e-07, 'Sig_13_0': 5.9207071659999999e-06, 'Sig_14_0': 1.2224001670000001e-07, 'Sig_22_0': 3.6622825020000002e-09, 'Sig_23_0': 7.4141336339999994e-08, 'Sig_24_0': 1.495491124e-09, 'Sig_33_0': 3.165637487e-06, 'Sig_34_0': 7.9058234540000002e-08, 'Sig_44_0': 2.040387648e-09}
More info at: https://github.com/SixTrack/SixTrack/issues/267#issuecomment-307333656
S-matrix transformation to un-coupled frame
Input sigma matrix:
Original
Corrected
Checked using full SixTrack simulations (numerical divergence of the computed kicks)
K. Sjobaek

## Slide 45
Outline
Introduction
  SixTrack
  Beam-beam effects in SixTrack
  Review of the 6D beam-beam routines
Numerical model
  Transverse generalized kicks
  Linear coupling treatment
  Energy change
Performed tests
  Overview
  Boost/anti-boost
  Linear coupling
What next

## Slide 46
We want to move from the monolithic structure of the SixTrack FORTRAN code into a much more flexible tool
The idea is to bring the knowledge from the SixTrack experience into a modern modular library called SixTrackLib aiming at:
  Better integration with other simulation and analysis tools (via a python interface)
  Improving efficiency of further development and maintenance
  Retaining SixTrack computational efficiency (core routines written in C)
  Profiting of huge computing power offered by GPU computing (via OpenCL)
What next
Thanking with beam-beam on GPU already exploited for FCC studies using a simplified model (linear map + head-on kicks)  extremely promising (more info on S. Furuseth’s thesis)
Next challenge will be to keep a significant speed-up while tracking the full LHC lattice with all long-range and head-on encounters
Plan to have first pilot studies by the end of 2018
S. Furuseth, X. Buffat

## Slide 47
Thanks for your attention!

## Slide 48
Next steps
We want to move from the monolithic FORTRAN structure of SixTrack into a much more flexible tool
The idea is to bring the knowledge from SixTrack experience into a modern modular library called SixTrackLib aiming at:
  Better integration with other simulation and analysis tools (via a python interface)
  While retaining SixTrack computational efficiency (core routines written in C)
  Profiting of huge computing power offered GPU computers (via OpenCL)