## Slide 1: Head-on beam-beam compensation in RHIC
W. Fischer, X. Gu, K.A. Drees, C. Liu, Y. Luo, A. Marusic, R. Michnoff, T.A. Miller, M. Minty, C. Montag, A.I. Pikin, G. Robert-Demolaize, V. Schoefer, P. Thieberger, and S.M. White
[Phys. Rev. Accel. Beams 20, 091001 (2017)]
ICFA Mini-Workshop on Beam-beam Effects in Circular Colliders
5-7 February 2018, LBNL
r
r’
Yellow electron lens
Principle
Notes: 30 min = 25 slides

## Slide 2: Contents
Principle of head-on beam-beam compensation
  History at DCI (Orsay, 1970s)
Implementation at RHIC
  Lattice design and verification
  RHIC e-lens technology => presentation by Xiaofeng Gu
Tune distribution widths with e-lenses
Operational use in 2015
  Luminosity gain
  Impact on beam loss rate, emittance growth, background

## Slide 3: Peer-reviewed references RHIC HOBBC
X. Gu, M. Okamura, A. Pikin, W. Fischer, and Y. Luo, "The effects of realistic pancake solenoids on particle transport", Nucl. Instrum. and Methods A 637, pp.190-199 (2011).
Y. Luo, W. Fischer, N.P. Abreu, X. Gu, A. Pikin, and G. Robert-Demolaize, "Six-dimensional weak-strong simulation of head-on beam-beamcompensation in the Relativistic Heavy Ion Collider", Phys. Rev. ST Accel. Beams 15, 051004 (2012).
X. Gu, F.Z. Altinbas, E. Beebe, W. Fischer, B.M. Frak, D.M. Gassner, K. Hamdi, J. Hock, L. Hoff, P. Kankiya, R. Lambiase, Y. Luo, M. Mapes, J. Mi, T. Miller, C. Montag, S. Nemesure, M. Okamura, R.H. Olsen, A.I. Pikin, D. Raparia, P.J. Rosas, J. Sandberg, Y. Tan, C. Theisen, J. Tuozzolo, and W. Zhang, ”The electron lens test bench for the relativistic heavy ioncollider at Brookhaven National Laboratory”, Nucl. Instrum. and Methods A 743, pp. 56-67 (2014).
W. Fischer, X. Gu, Z. Altinbas, M. Costanzo, J. Hock, C. Liu, Y. Luo, A. Marusic, R. Michnoff, T.A. Miller, A.I. Pikin, V. Schoefer, P. Thieberger, and S.M. White, "Operational head-on beam-beam compensation with electronlenses in the Relativisitc Heavy Ion Collider", Phys. Rev. Lett. 115, 264801 (2015).
X. Gu, Z. Altinbas, M. Costanzo, W. Fischer, D.M. Gassner, J. Hock, Y. Luo, T. Miller, Y. Tan, P. Thieberger, C. Montag, and A.I. Pikin, "Tansverse profile of the electron beam for the RHIC electron lenses", Nucl. Instrum. and Methods A 798, pp. 36-43 (2015).
Y. Luo, W. Fischer, and S. White, "Analysis and modeling of proton beam loss and emittance growthin the Relativisitc Heavy Ion Collider", Phys. Rev. Accel. Beams 19, 021001 (2016).
P. Thieberger, Z. Altinbas, C. Carlson, C. Chasman, M. Costanzo, C. Degen, K. A. Drees, W. Fischer, D. Gassner, X. Gu, K. Hamdi, J. Hock, A. Marusic, T. Miller, M. Minty, C. Montag, Y. Luo, A.I. Pikin, and S.M. White, "High energy Coulomb-scattered electrons for relativisticparticle beam diagnostics", Phys. Rev. Accel. Beams 19, 041002 (2016).
X. Gu, W. Fischer, Z. Altinbas, M. Anerella, E. Bajon, M. Bannon, D. Bruno, M. Costanzo, A. Drees, D. M. Gassner, R. C. Gupta, J. Hock, M. Harvey, A.K. Jain, J.P. Jamilkowski, P. Kankiya, R. Lambiase, C. Liu, Y. Luo, M. Mapes, A. Marusic, C. Mi, R. Michnoff, T.A. Miller, M. Minty, S. Nemesure, W. Ng, D. Phillips, A. I. Pikin, P.J. Rosas, G. Robert-Demolaize, T. Samms, J. Sandberg, V. Schoefer, T.C. Shrey, Y. Tan, R. Than, C. Theisen, P. Thieberger, J. Tuozzolo, P. Wanderer, W. Zhang, and S. M. White, "Electron lenses for head-on beam-beam compensation in RHIC", Phys. Rev. Accel. Beams 20, 023501 (2017).
W. Fischer, X. Gu, K.A. Drees, C. Liu, Y. Luo, A. Marusic, R. Michnoff, T.A. Miller, M. Minty, C. Montag, A.I. Pikin, G. Robert-Demolaize, V. Schoefer, P. Thieberger, and S.M. White, "Compensation of head-on beam-beam induced resonance drivingterms and tune spread in the Relativistic Heavy IonCollider", Phys. Rev. Accel. Beams 20, 091001 (2017).

## Slide 4: History of head-on beam-beam compensation (HOBBC)
Head-on compensation schemes [S. Peggs, Handbook (1999); J.P. Koutchouk, V. Shiltsev, Handbook (2013)]:
Direct space charge compensation (4 beams)
Indirect space charge compensation (electron lenses)
Resonance compensation between interaction points (not implemented)
Octupoles for reduction of nonlinearities (VEPP-4, no clear improvement)
Reduction of BB resonance strength with crab-waist (DAFNE, SuperKEKB)
Proposals/studies of direct/indirect space charge compensation:
COPPELIA ⇒ 4-beam (J.E. Augustine, HEACC, 1969)
DCI ⇒ 4-beam (G. Arzelia et al., HEACC, 1971) ⇒ only operational attempt before RHIC
CESR ⇒ e-lens (R. Talman, unpublished, 1976)
SSC ⇒ e-lens (E. Tsyganov et al., SSCL-PREPRINT-519 ,1993)
LHC ⇒ e-lens (E. Tsyganov et al., CERN SL-Note-95-116-AP, 1995)
Tevatron ⇒ e-lens (Shiltsev et al., PRST-AB, 1999)
e+e- collider ⇒ 4-beam (Y. Ohnishi and K. Ohmi, Beam-Beam’03, 2003)
RHIC ⇒ e-lens (Y. Luo, W. Fischer, BNL C-A/AP/286, 2007) ⇒ implementation in 2015
FCC-hh ⇒ e-lens? (no head-on limit observed in the LHC)

## Slide 5: Head-on beam-beam compensation Principle
Correction in same turn, need to fulfill 2 conditions:
(1) kp phase advance minimizes beam-beam resonance driving terms – implemented with ATS type lattice [Y. Luo et al., PRSTAB 15, 051004 (2012);]
(2) Same amplitude correction kick as bb kick reduces beam-beam tune spread – implemented with electron lenses (not possible with magnets)

## Slide 6: Head-on beam-beam compensation Principle
Beam-beam kicks:
<= effect of Gaussian p-beam on proton
<= effect of Gaussian e-beam on proton
Matching condition implies:
<= electron lens current
<= matched beam-beam parameters

## Slide 7: Head-on beam-beam compensation in DCI
Operational head-on beam-beam compensation was only tested in DCI (starting in 1976) – 4-beams (e+e−e+e−)
Main parameters:
  Circumference 94.6 m
  Energy 1.8 GeV
  Beam-beam x ~0.05-0.1
  Luminosity (design) ~1032 cm-2s-1
Luminosity fell short by ~100x compared to expectations (2-, 3-, and 4-beam L about the same)
The Orsay Storage Ring Group, “Status report on D.C.I.”, PAC77
The Orsay Storage Ring Group, “Status report on D.C.I.”, PAC79
DCI Hall, LAL Orsay
Limited by unanticipated coherent motion of e+ and e− beams
Notes: References:
- Ya. S. Derbenev, “Collective instability of compensated colliding beams”, Nuclear Physics Institute, Siberian Division, Academy of Sciences USSR, Novosibirsk, Report No IYAF 70-72, in Russian (1972), SLAC-TRANS 151 in English.
- N.N. Chau and D. Potau, “Stabilité des oscillations transverse dans un anneau à charge d’espace compensée”, LAL Orsay (1974 and 1975).
- B. Podobedov and R.H. Siemann, “Coherent beam-beam interaction with four colliding beams”, Phys. Rev. E 52, No 3, pp. 3066-3073 (1995).

## Slide 8: Implementation at RHIC Overview
[X. Gu et al., PRAB 20, 023501 (2017), presentation X. Gu]
Dy = kp
<= RHIC electron lenses (based on Tevatron lenses and RHIC EBIS) with 2 solenoids of opposite polarity coupling and spin effect are compensated locally

## Slide 9: Implementation at RHIC Lattice design
Lattice requirements:
Phase advance between IP8 and e-lenses kp (k integer)
Large b-function (beam size) at e-lens
  easier alignment with large beams
  better stability with large beams found marginal stability in simulations at 255 GeV [S. White, CERN, Report No. CERN-2014-004, 2014, p. 133] test with Au and 1.5 T solenoid field found better stability than in simulation
Small nonlinear chromaticity
  correlates with large DA (simulations by Yun Luo)
approx. stability threshold [A. Burov, PRE 59, 3605 (1999)]

## Slide 10: Implementation at RHIC Lattice design
ATS lattice for Blue ring
b-wave over 2 IPs [S. Fartoukh, PRSTAB 16, 111002 (2013); S. White BNL-105550-2014-IR, C-A/AP/519 (2014)]
Nonlinear chromaticity smaller in all planes
except Blue vertical (still smaller than Yellow 2012)

## Slide 11: Implementation at RHIC Lattice verification
Blue hor: 11.7% rms
measured beta-beat
Blue ver: 12.1% rms
Yellow hor: 11.7% rms
Yellow ver: 14.1% rms
significant discrepancy for Yellow nonlinear chromaticity

## Slide 12: E-lens orbit and tune effect Linear effects
[Simon White]
Tune and orbit change due to vertical displacement with Au beam

## Slide 13: Tune distribution width BTF measurement
Use Beam Transfer Function measurement for widths of distribution:
observe beam response <x> to small transverse harmonic excitation Acos Wt around betatron tune W [A. W. Chao, Physics of collective …”, Ch. 5 (1993)] :
Complex response function R(W) := CR(W) + iCI(W)
Width of tune distribution: Non-zero r(W) if non-zero Im(R)/(R) (Note: shape of R(W) has more information – under investigation by Yun Luo)
coherent beam response <x>
excitation frequency W
tune distribution r(W)
RHIC BTF application

## Slide 14: Tune distribution width Expectation
BB tune shift at amplitude a
BB tune spread from zero to amplitude a
total tune spread from zero to amplitude a, assuming Q0 and Qbb are uncorrelated
few particles at large amplitudes a – resulting in small BTF signal
maximum amplitude a with detectable BTF signal not known a priori

## Slide 15: Tune distribution width e-beam current and size
e-lens current scan
e-lens size scan
Measured tune widths match expectation for a <= 2.5 sp

## Slide 16: Tune distribution width with collisions BTF
Limitation: Coherent BB modes prevent extraction of incoherent tune distribution widths. Successful in simulation [P. Görgen et al., NIMA 777, 43-53 (2015)], not with RHIC data.
s-modes
s-modes
p-modes
p-modes
1x BB
2x BB
No observable change in tune distribution width with e-lens
Can suppress coherent modes with tune separation, done in operation with p+Al, p+Au collisions (Qp ~ 0.68, QA ~0.23)

## Slide 17: Tune distribution width BB footprint compression
Measured tune widths match expectation for a <= 3.5 sp
no BB
2x BB
compression
=> Demonstrated beam-beam generated footprint compression with election lens
e-lenses can only compress BB generated tune spread, not from other source (e.g. Q’ and dp/p)
Further increase in e-lens current will increase tune spread again

## Slide 18: Operational use in 2015 collisions at 2 experiments
e-lens e-beam currents
backscattered electron rates
e-lenses turn on before collision (112 stores with both lenses without a single turn-on failure)
Beams into collision at PHENIX, collimators to store positions (requires PHENIX collisions)
Beams into collision at STAR and e-lenses e-lenses prevent emittance growth for large bb param. x
Lenses are gradually turned off when lattice alone can sustain bb parameter x
eBSD rate [Hz]
IPM emittances
luminosities
1
2
3
3
3
4

## Slide 19: Luminosity p+p at 100 GeV 2012 vs in 2015
2012: without HOBBC Lavg not increasing any more with increase in Nb
2015: with HOBBC Lavg increasing with Nb
Average store luminosity saturated in 2012 despite increase in bunch intensity.

## Slide 20: Luminosity p+p at 100 GeV 2012 vs in 2015
Luminosity increase Lavg : +91% (measured)
2/3 from lattice alone, 1/3 from e-lens (calculated from measured xp values)
Increase in bb parameter xp from e-lens: +38%(measured)
Note: possible that
higher beam-beam parameters can be demonstrated in the
future in all situations, thereby changing the relative gains.

## Slide 21: Effect of e-lenses on beam loss rate, emittance growth
Beam loss rate 1/t2
Hor. emittance
Ver. emittance
Additional beam loss rate: 0.5-1.0%/h
Additional emittance growth:
6% over full store length (~3% avg.)
fast slow
2 stores Yellow e-lens on for 6.75 & 5.28 h respectively (other stores 0.45–1.83 h)

## Slide 22: Effect of e-lenses on experimental background
2 stores Yellow e-lens on for 6.75 & 5.28 h respectively (other stores 0.45–1.83 h)
Scintillator N2 indicative of machine generated background from Yellow beam
Background rate (PHENIX N2):
  2-3x higher with e-lens (2015 background rates 3-4x smaller than 2012, despite L 2x higher)
  acceptable

## Slide 23: Further experiments with electron lenses
PHENIX experiment rebuilt into sPHENIX next polarized proton operation only after sPHENIX compeletion (>2023)
Instability test at higher energy 255 GeV – smaller beam size unstable in simulations (S. White, BB2013) => may require damper
eRHIC stepwise e-bunch replacement => presentation Christoph Montag
Hollow e-lens tests in 2018 => HL-LHC collimation improvements, presentation Adriana Rossi

## Slide 24: Summary Head-on beam-beam compensation in RHIC
First successful operational implementation of head-on beam-beam compensation, 39 years after DCI 4-beam scheme
  New ATS-type lattice (Dy = kp)
  E-lenses build and commissioned
Demonstrated beam-beam generated footprint compression with e-lens
2x luminosity gain gain with new head-on beam-beam compensation scheme 2/3 of gain from lattice alone, 1/3 from e-lens
Measured detrimental effects of e-lens on beam loss rate (0.5-1.0%/h), emittance growth (+6% over 8h stores) and background (+2-3x, acceptable)

## Slide 25: Acknowledgements
Brookhaven National Laboratory
Z. Altinbas, M. Anerella, M. Bai, E. Bajon, M. Bannon, D. Bruno, M. Costanzo, C.D. Dawson, A. Drees, B. Frak, G. Ganetis, D.M. Gassner, R.C. Gupta, P. Joshi, J. Hock, K. Hock, M. Harvey, L. Hoff, A.K. Jain, J.P. Jamilkowski, P. Kankiya, P. Kovach, R. Lambiase, K. Mirabella, M. Mapes, A. Marone, K. Mernick, J. Muratore, C. Mi, S. Nemesure, W. Ng, D. Phillips, A.I. Pikin, P.J. Rosas, T. Samms, J. Sandberg, T.C. Shrey, L. Snydstrup, S. Tepikian, Y. Tan, R. Than, C. Theisen, J. Tuozzolo, P. Wanderer, W. Zhang Groups of BNL Collider-Accelerator Department BNL Superconducting Magnet Division STAR and PHENIX experiments – supported parasitic commissioning
Institutions
FNAL: TEL experience, beam-beam experiments and simulations US LARP: beam-beam simulation CERN: beam-beam experiments and simulations
Individuals H.-J. Kim, V. Shiltsev, T. Sen, G. Stancari, A. Valishev, G. Kuznezov, FNAL; G. Kuznezov, BINP; X. Buffat, R. DeMaria, W. Herr, J.-P. Koutchouk, F. Schmidt, F. Zimmermann, CERN; U. Dorda, DESY; T. Piloni EPFL; N. Milas, ESS; V. Kamerdziev, FZJ; K. Ohmi, KEK, J. Qiang, LBNL; A. Kabel (formerly SLAC); P. Goergen, (formerly TU Darmstadt)