## Slide 1
The RHIC electron lenses - technology and e-beam measurements
February. 05 ~ February. 07, 2018
The ICFA Mini-Workshop on Beam-Beam Effects in Circular Colliders
Xiaofeng. Gu, W. Fischer, Z. Altinbas, M. Anerella, E. Bajon, M. Bannon, D. Bruno, M. Costanzo, Drees, D. M. Gassner, R. C. Gupta, J. Hock, M. Harvey, A. K. Jain, J. P. Jamilkowski, P. Kankiya, R. Lambiase, C. Liu, Y. Luo, M. Mapes, A. Marusic, C. Mi, R. Michnoff, T. A. Miller, M. Minty, S. Nemesure, W. Ng, D. Phillips, A. I. Pikin, P. J. Rosas, G. Robert-Demolaize, T. Samms, J. Sandberg, V. Schoefer, T. C. Shrey, Y. Tan, R. Than, C. Theisen, P. Thieberger, J. Tuozzolo, P. Wanderer, and W. Zhang
Thank the Committee for invitation!

## Slide 2
Outline
Introduction
Technology
e-beam Measurement
Summary

## Slide 3
RHIC
STAR
6:00 o’clock
PHENIX
8:00 o’clock
E-lens
10:00 o’clock
RHIC – a High Luminosity (Polarized) Hadron Collider
LEReC 2:00 o’clock

## Slide 4
V. Shiltsev, A. Burov, A. Valishev, G. Stancari, X.-L. Zhang, et al.
2 lenses in Tevatron:
Solenoid field 6 T
Solenoid length 2.7 m
e-beam energy 5/10 kV
e-beam current 0.6/3 A (pulsed)
Fermilab Tevatron E-lens
BNL Electron Beam Ion Source
J. Alessi, E. Beebe, D. Raparia, M. Okamura, A. Pikin et al.
Ion source for RHIC:
Solenoid field 5 T
Solenoid length 2 m
e-beam energy 20 kV
e-beam current 10 A (pulsed)
RHIC e-lens
6 T (±50 mm straight)
2 m
10 kV
1 A (pulsed&DC)
Introduction -- Technology

## Slide 5
p
p
electron gun
electron collector
SC main solenoid B = 6 T, I = 440 A + 16 more magnets (fringe fields, correctors)
orbit steerers
orbit steerers
e−
e−
e−
warm solenoids
warm solenoids
Introduction –One E-lens Layout
Gaussian Beam
1A DC current
78 kHz pulsed beam
5~10 keV
Features:
Independent beam size control
Transvers beam position control
[Wolfram Fischer et al., Phys. Rev. Accel. Beams 20, 091001, 2017]
[Wolfram Fischer et al., PRL 115, 264801 (2015)]

## Slide 6
Introduction – Instrumentation and Beam control
BPM (e & p)
eBSD Detector
Anode Voltage M
YAG screen
Collector & Sensor
CTs
Ion Collector
Drift Tubes
[Xiaofeng Gu et al., Phys. Rev. Accel. Beams 20, 023501, 2017]
Cathode profile->Beam profile
Anode Voltage->Beam Current
Cathode Bias-> Beam Energy
GSX&Y>Beam Position
SLCX&Y>Beam Angle
GS1/Solenoid-> Beam Size

## Slide 7
Introduction – Two Lenses Layout
+6 T
−6 T
Top view
Side view

## Slide 8
Outline
Introduction
Technology
e-beam Measurement
Summary

## Slide 9
E-gun Design for 100GeV and 250GeV Proton
Thermal cathode
IrCe (above) and Tungsten (below)
Minimize error between simulated profile and Gaussian Profile
[Xiaofeng Gu et al., NIMA, Volume 743 (2014)]
100GeV
250GeV
Cathode
Anode
Control electrode
Drift tube

## Slide 10
The electron beam has to have Gaussian profile with r/σ≈3: overlapping the proton beam .
Chart: Radial profile of emission current density for U_a=7.27kV, U_contr=0.0V, I_el=0.601A, Alfa=5.76, Beta=-0.0031, Sigma=1.276 mm
Chart: Emission current density radial profiles for zero control voltage and different anode voltages
Chart: Emission current density radial profiles for U_a=8.8kV and different voltages on the control electrode
Courtesy of A.I. Pikin
E-gun Simulation With Model
Cathode Profile

## Slide 11
Collector Design
Yellow E-lens
Collector
Reflector (open path for camera)
Ion collector (movable)
Water cooling
Magnetic shield
[Xiaofeng Gu et al., NIMA, Volume 743 (2014)]
8 RTD

## Slide 12
E-Beam Instrumentation System
Beam Alignment : BPM (2) (also for p-beam), Backscattered electron monitor(1)
E-beam Current : BCT (4), e-beam Loss (drift tubes)
E-beam Profile : YAG Screen (1), Pin-hole detector (1)
Ion Current : Ion collector (1)
Collector Temperature: RTD (8)
BPM
Instrumentation System
[Toby Miller et al., IBIC2014 mopf08]

## Slide 13
YAG, Pinhole and Scrapers
Yellow E-lens
[Xiaofeng Gu et al., NIMA, Volume 743 (2014)]
Scrapers (alignment to collector)
YAG screen
Pinhole Scanner
Collector potential > 0

## Slide 14
Electron beam backscattering detector (eBSD)
Solenoid #1 In tunnel
Yellow E-lens
[Peter Thieberger et al., Phys. Rev. Accel. Beams 19, 041002, 2016]

## Slide 15
Timing and modulator design
Yellow E-lens
50nS
100nS
[Yugang Tan et al., DOI: 10.1109/PPC.2013.6627405
RHIC Beam: 360 bucket, 111 bunches, 1 bunch occupies 3 bucket; 30 empty bucket for beam abort gap; the last bunch bucket number is 331;
DC mode: The electron beam is always ON. DC mode is used for beam-beam compensation operation;
Parasitic mode: the electron beam can be run within RHIC beam abort gap during physics store, from 2 Hz to 78 kHz. That means more hardware commissioning time for e-lens.
Pulse mode: When there is NO RHIC beam, the pulse mode electron beam pulse length can be changed up to 500 mS.

## Slide 16
Superconducting Solenoid Design
6T field
Field straightness (10 short correctors)
Angle correctors (2)
2.8 m long total
Fringe solenoid
[Ramesh Gupta et al., PAC2011 pp. 1130-1132]

## Slide 17
Superconducting magnet
winding at BNL 22 layers, ~25000 turns
shell with correctors
End preparation
Solenoid #1 In tunnel
Yellow E-lens
[J. Muratore et al., IEEE Trans. Appl.Supercond. 24, 4100505 (2014)]
[M. Anerella et al., IEEE Trans. Appl.Supercond. 24, 4101804 (2014)]

## Slide 18
Superconducting Magnet
Tolerance ± 50 mm
±1000 mm good field
Operated at 6T.
A maximum ±50 mm deviation of the main solenoid field lines within ±800 mm
Courtesy of A. Jain
Needle & mirror
Vibrating Wire
[A. Jain, Proceedings of the International Magnetic Measurement Workshop 2015, Hsinchu, Taiwan]

## Slide 19
Outline
Introduction
Technology
e-beam Measurement
Summary

## Slide 20
Electron Beam Measurement
1A Current
DC or pulsed
Anode Voltage
Electron Beam
Two cathode sizes

## Slide 21
Electron beam profile measurement (2014)
YAG screen
Pinhole Detector
Current 70 mA
Beam profile from YAG is a Gaussian
Profile does not change with current
Current 1150 mA.
Pinhole profile is Gaussian
[Xiaofeng Gu et al., NIMA, Volume 798, p36-43 (2015)]

## Slide 22
NO RHIC ion beam
Blue and Yellow were running simultaneously
Beam current was 1 A
Blue was running for 9.5 hours during 2013 commissioning.
Blue DC 1A electron beam
Yellow DC 1A electron beam
DC beam

## Slide 23
Modulator current indicates 78 kHz is running.
Blue and Yellow were running 78 kHz pulse mode with 1A simultaneously within RHIC beam abort gap;
Parasitic to RHIC beam provides more commissioning time;
Blue e-lens 78 kHz was running for 14 hours;
RHIC ion beam
Blue 78 kHz 1A electron beam
Yellow 78 kHz 1A electron beam
Parasitic Mode Electron Beam

## Slide 24
Two methods to do transverse position and angle alignment: BPM or eBSD (detector)
BPMs in both lenses to bring e-beam and ion beam for overlap (transverse and angle)
Backscattered electron detector to maximize overlap (transverse and angle)
eBSD, ion beam scan
e-BPMs, E-beam scan
Transverse e-Beam Alignment

## Slide 25
Longitudinal alignment
Yellow E-lens

## Slide 26
Example of Alignment

## Slide 27
Outline
Introduction
Technology
e-beam Measurement
Summary

## Slide 28
Summary
Two e-lenes were built at BNL, according to Fermilab Tevatron E-lens and BNL EBIS technology.
These low risk technologies are used for beam current, profile, size, energy, positon and angle control and measurement.
The e-beam parameters are satisfied with beam-beam compensation requirement.
eBSD was developed and used for beam alignment.
The two e-lenes were operated although RHIC 2015 run. The head-on beam-beam compensation scheme, consisting of new lattice (RDT compensation) + e-lenses (DQ compensation) result: Lpeak +150% Lavg +90%

## Slide 29
Acknowledgements
Brookhaven National Laboratory
M. Anerella, M. Bai, C.D. Dawson, A.K. Drees, B. Frak, G. Ganetis, D.M. Gassner, R.C. Gupta, P. Joshi, K. Hock, L. Hoff, P. Kovach, R. Lambiase, K. Mirabella, M. Mapes, A. Marone, A. Marusic, K. Mernick, M. Minty, C. Montag, J. Muratore, S. Nemesure, S. Plate, G. Robert-Demolaize, L. Snydstrup, S. Tepikian, C.W. Theisen, J. Tuozzolo, P. Wanderer, W. Zhang STAR and PHENIX experiments – supported e-lens commissioning
Institutions
FNAL: TEL experience, beam-beam experiments and simulations US LARP: beam-beam simulation CERN: beam-beam experiments and simulations
Individuals H.-J. Kim, V. Shiltsev, T. Sen, G. Stancari, A. Valishev, G. Kuznezov, FNAL; G. Kuznezov, BINP; X. Buffat, R. DeMaria, J.-P. Koutchouk, T. Pieloni, F. Schmidt, F. Zimmermann, CERN; V. Kamerdzhiev, FZJ; A. Kabel, SLAC; P. Goergen, TU Darmstadt