## Slide 1: RD53A Emulator Demo
By Douglas Smith

## Slide 2: What is it?
It is a digital emulator of the RD53A chip.
  Written in Verilog
  Targeted to FPGAs(KC705)
Designed by ACME lab at UW
Work of numerous graduate and undergraduate students
Emulator outline shown on right

## Slide 3: Motivation 1
Original use cases
  (1): Act as stand in for real chip
  (2): Early debugger for readout systems under development
The real chip was released and most interest groups now have an RD53A
Use case shifted to producing realistic hit data

## Slide 4: Motivation 2
Not every lab has an onsite particle accelerator or an easy way to excite the chip. Most of the data being collected is not interesting.
Use Case (1): Produce realistic hit data.
  Resembles what would be produced if the RD53A was put into the LHC.
Accomplished by studying actual data collected at CERN.
  Analyzed the data using clustering/line detection
It was determined most of the hit data consisted of simple Tetris pieces or lines.
Having realistic hit data useful for debugging

## Slide 5: Motivation 3
Use Case (2): General debugging and a point of comparison.
  The RD53A is a black box.
  The emulator is easier to look inside and debug for issues.
Use Case (3): The emulator easily modifiable.
  Bugs fixed on a much shorter timescale than developing a new chip
  New features can be added
Use Case (4): Starting point for new interest groups for initial testing and debugging.

## Slide 6: Current Features
Input data is properly received.
  The emulator receives 160 Mbps data.
  Correctly performs synchronization/channel alignment.
Input frames are properly decoded using rd53a protocol into commands, triggers, and data
Output data of the emulator is properly encoded using the aurora 64/66B protocol
  640 Mbps over four lanes.
  Custom implementation that uses Xilinx SERDES modules.

## Slide 7: Current Features 2
Reading/writing of global registers works.
  The read out registers are sent through lane 0.
  Auto read sent when there is no data.
Trigger commands
  Properly stored/responded too triggers outputting clumps of realistic hit data.
  Formatting follows the RD53A protocol.
Large amount of configurability
The output level of the hit data is controllable by a configuration register.

## Slide 8: Limitations
RD53A features that involve analog circuitry have been greatly simplified or removed entirely.
  Simplification: Pixels are represented by large block, not individual emulated pixels
  Removed: Calibration and writing to pixels
A 160 MHz input clock is required as an input.
  Don’t perform CDR
ECR, BCR, and CAL commands are received but have no external impact.

## Slide 9: Readout Systems
Recently, a large portion of the effort at UW has been establishing communication with various readout systems for the RD53A.
The emulator isn’t particularly useful if it can’t communicate with the DAQ readout systems.
The three big readout systems we have been working on are YARR, RCE and FELIX.

## Slide 10: YARR
YARR developed by LBNL
  Timon Heim spearheading the project
The emulator has established communication with a slightly modified YARR.
  Rearranging the clocks on the YARR side.
  Added a counter to manage the Ohio MMC chip.
  Sent a 250 MHz clock was sent.
Required hardware
  Two KC705 Xilinx Board
  A VHDCI to FMC chip
  A VHDCI to Quad DP Rev A. chip
  The Ohio Multi Chip FMC
  Two SMI cables
  A mini-DP to mini-DP cable

## Slide 11: YARR 2
Features
  The YARR test suite, digital scan, analog scan, rd53a_readreg
  Communication at 640 Mbps
  Can configure the hit data generation rate
An example of data received with the YARR setup at the UW.
Shows both high data generation rate and low data generation rate

## Slide 12: RCE
Required hardware
  HSIO2/DTM + FEB ( HSIO2 is a standalone RCE system)
  PC + 10G-Eth card
  FEB
Features
  The same functionality as with YARR is supported
  160 Mbps communication
Setup at UW is not the full setup, but consider close enough for debugging and testing purposes

## Slide 13: FELIX
Required hardware
  A VLDB board
  2 VC709 Xilinx Board
  TTC mezzanine card
  The Ohio Multi Chip FMC
  Two SMI cables
  A mini-DP to micro-HDMI cable
  4 optical cables
Features
  Not currently running at UW, but working hard on getting the system setup
Testing FELIX with a simpler PC

## Slide 14: Where next?
RD53A is completed at a high level perspective.
  Focus will shift to continuous support
  Bug fixing
  Adding additional features
Work will continue on the FELIX setup.
  A simple mock up of FELIX has worked.
  More work is required to get the system fully operational.
The next big direction of the project is the RD53B.

## Slide 15: System Demo
Website: https://rd53a-doc.readthedocs.io/en/latest/
Your feedback is highly appreciated and desired
Live demo
Questions?